## Slide 1
Yihua Zheng and Rebekah M. Evans
Solar Energetic Particles (SEPs)
Goals: identify SEPs in data, connect to drivers, identify characteristics of SEPs
June 3, 2014 SW REDI Boot Camp
Notes: LOOK FOR AN SVS MOVIE!

## Slide 2: SEPs – important source of space radiation: hard to predict

## Slide 3
What are they?
Definition:
Energetic charged particles (such as electrons and protons) traveling much faster than ambient particles in the space plasma, at a fraction of the speed of light (relativistic!).
They can travel from the Sun to the Earth in one hour or less!
The term “SEP” usually refers to protons.
Notes: An SEP event is an enhancement in the radiation evironment.
Summarize effects again.

## Slide 4
Why do we care?
Radiation hazards for spacecraft,
human in space and airline passenger safety
Notes: An SEP event is an enhancement in the radiation environment.
Summarize effects again.
For this effect and the biological/ human radiation risk hazard, we partner with the Space Rad Analysis Group NASA JSC.
Definition:
Energetic charged particles charged particles such as energetic electrons that are traveling much faster than ambient electrons in the space plasma and have the potential for causing ionizing radiation damage to spacecraft and

## Slide 5: Space Environments and Effects on Spacecraft
Plasma
Charging
Impacts
Drag
Surface
Erosion
Ultraviolet & X-ray
Neutral
gas particles
Particle
radiation
Micro-
meteoroids & orbital debris
Ionizing &
Non-Ionizing
Dose
Degradation of micro-
electronics
Degradation of optical components
Degradation of solar cells
Single
Event
Effects
Data corruption
Noise on Images
System shutdowns
Circuit damage
Degradation of thermal, electrical, optical properties
Degradation of structural integrity
Biasing of instrument readings
Pulsing
Power drains
Physical damage
Torques
Orbital decay
Structural damage
Decompression
Space Radiation Effects
Shaded in yellow
after J. Barth

## Slide 6
Solar energetic particles (SEPs)
Flares
Coronal Mass Ejections
Notes: At the SWRC, our goal is to monitor the space environment for NASA robotic mission operators.
For spacecraft outside of a protective planetary magnetosphere, the energetic particles very potential for damage.
The sources are both flares, CMEs. You remember that a flare is a rapid release of energy, which can be transferred to particles as kinetic energy. CMEs can drive shock waves, and shock waves are also efficient particle accelertors.

## Slide 7
7
SEPs: ion radiation storms
Potentially affect everywhere in the solar system
Courtesy: SVS@ NASA/GSFC
Notes: SEPs: applicable and potentially damaging everywhere that they have influence

## Slide 8
Charged particle motion* is confined by the magnetic field.
Magnetic fields guide SEPs
This means that the source is very important.
*in a substantially strong B
0°
-90°
+90°
Notes: ENLIL
Charged particles, when the magnetic field is above some certain threshold, are tied to magnetic field lines. They will propagate along the magnetic field lines.
As we discussed earlier, because the Sun rotates, the interplanetary magnetic field takes a spiral shape in the equatorial plane. Use these lines to see where the soure regions can be for these spacecraft.
Just flares/source region connection

## Slide 9
Magnetic fields guide SEPs
This means that the source is very important.
*in a substantially strong B
0°
-90°
+90°
Charged particle motion* is confined by the magnetic field.
Notes: ENLIL
Charged particles, when the magnetic field is above some certain threshold, are tied to magnetic field lines. They will propagate along the magnetic field lines.
As we discussed earlier, because the Sun rotates, the interplanetary magnetic field takes a spiral shape in the equatorial plane. Use these lines to see where the soure regions can be for these spacecraft.
Just flares/source region connection

## Slide 10
Magnetic fields guide SEPs
This means that the source is very important.
*in a substantially strong B
0°
-90°
+90°
Charged particle motion* is confined by the magnetic field.
Notes: ENLIL
Charged particles, when the magnetic field is above some certain threshold, are tied to magnetic field lines. They will propagate along the magnetic field lines.
As we discussed earlier, because the Sun rotates, the interplanetary magnetic field takes a spiral shape in the equatorial plane. Use these lines to see where the soure regions can be for these spacecraft.
Just flares/source region connection

## Slide 11
Magnetic fields guide SEPs
This means that the source is very important.
*in a substantially strong B
0°
-90°
+90°
Charged particle motion* is confined by the magnetic field.
Notes: ENLIL
Charged particles, when the magnetic field is above some certain threshold, are tied to magnetic field lines. They will propagate along the magnetic field lines.
As we discussed earlier, because the Sun rotates, the interplanetary magnetic field takes a spiral shape in the equatorial plane. Use these lines to see where the soure regions can be for these spacecraft.
Just flares/source region connection

## Slide 12
Magnetic field lines are the road for charged particles
CMEs Can Widen Longitudinal Extent of SEP Events
Notes: If particles do not easily cross from one magnetic field line to another, it may seem like all SEP events would then be very narrow in longitude.
However, a CME can play a role not only in accelerating the particles, but also in distributing them over a wide range of longitudes, as we can see here in this simulation.
Here is a simulation that shows us what that might look like.
So, remember, when there is a cme, it can widen the area of the SEPs.

## Slide 13
CMEs Can Widen Longitudinal Extent of SEP Events
Notes: If particles do not easily cross from one magnetic field line to another, it may seem like all SEP events would then be very narrow in longitude.
However, a CME can play a role not only in accelerating the particles, but also in distributing them over a wide range of longitudes, as we can see here in this simulation. Sandro said how CMEs can be greater than 100 in width, so it is possible for the same SEP event to be seen at multiple locations.
Here is a simulation that shows us what that might look like.
So, remember, when there is a cme, it can widen the area of the SEPs.

## Slide 14
How Do We Monitor SEP Levels?
Track the particle flux at different locations.
Flux units: pfu, pfu/MeV
  Heliosphere with STEREO In-situ Measurements of Particles and CME Transients (IMPACT)
    Differential energy band; Units measured, some energy ranges are:
  Upstream of Earth with SOHO/COSTEP
    Units measured, some energy ranges are:
  Geostationary Orbit with GOES
    Integral flux, Units measured, some energy ranges are: pfu particle flux unit
Another useful quantity:
Fluence = flux integrated over the entire event.
Important for biological effects (flights)
(1 pfu = 1 particle flux unit= 1/cm^2/sec/sr)
Notes: Converting between the two is important to know in order to quantify the relative strengths.

## Slide 15
Event magnitudes:
  > 10 MeV/nucleon integral fluence: can exceed 109 cm-2
  > 10 MeV/nucleon peak flux: can exceed 105 cm-2s-1
SEP Intensity

## Slide 16
PARTICLE SNOW!
Coronagraph acting as particle detector 
SDO AIA 131 Å + SOHO/LASCO C2
May 17 02:00 UT
SOHO/LASCO C3
May 17 03:00 UT
One hour later
Flare peaked at 01:47 UT
Notes: Another way that we “see” SEPs are in images, for example, coorngraphs. Here you can see the ‘snow’ of particles hitting the detector.

## Slide 17
How do we define an SEP Event?
SWRC: SEP event detections are defined as:
GOES Proton E > 10 MeV channel > 10 pfu
GOES Proton E > 100 MeV channel > 1 pfu
Notes: Here is an example of an event where the 10 MeV limit was met, but not the 100 MeV.
SOHO: > 15.8 MeV proton channels 0.1 pfu/MeV.

## Slide 18
How Do We Quantify an SEP Event?
Notes: Fluence is also important

## Slide 19: Human Safety in Space
GCR
SEP
Johnson Space Center/Space Radiation Analysis Group (SRAG)
Limit: the > 100 MeV flux exceeding 1pfu
(1 pfu = 1 particle flux unit= 1/cm^2/sec/sr)
All clear (EVA –extravehicular activity)

## Slide 20
Can we predict SEP events?
REleASE Model
Uses detection of high energy *electrons* to predict arrival of high energy *protons*
Data source: SOHO COSTEP
Notes: http://iswa.gsfc.nasa.gov/wiki/index.php/SOHO/Costep_Proton_Flux_-_Forecast

## Slide 21
How Often Do SEP Events Occur?
SEP event detections in the near-Earth environment
(GOES 13, Proton E > 10 MeV channel)
Total Events
2012
2011
2010
2007-2009: Zero Events - Solar Minimum Indeed!
Since March 2011
STEREO A: 16
STEREO B: 11
2013 (Jan-May)
Notes: If you are speaking about one specific location in the heliosphere, for example, just at the Earth, then during solar minimum, there can be only a few or even none in a year. During higher activity times, there can be about one per month or so.
However, there can be many more SEP events happening at other locations, or that we simply are not measuring – remember how that sometimes events can be focused in space!
With only four events in the first 5 months of 2013, things are a little more quiet than we would have guessed.

## Slide 22
Recognizing profile shapes of SEP flux and associating it with the source/driver

## Slide 23
Impulsive: The “peak at the beginning due to flare, fall off” – indicates how well connected you are to the source (timing)

## Slide 24
Gradual: The “jump up from flare, slow rise
Then peak when the ICME passes the spacecraft”

## Slide 25
The “slow rise then peak, (slow rise can let you know that you are not well connected
ICME doesn’t hit spacecraft so falls off”

## Slide 26
The “multiple event weirdness”

## Slide 27
July 23 flare as seen in STEREO A EUVI 195
Increase of more than 5 orders of magnitude at STEREO A
SEP event also detected by GOES, and later enhancement seen at STEREO B (possibly due to IPS)
July 23, 2012
Example where is reaches one spacecraft, then later another…
Notes: On July 23rd it really put on a show.

## Slide 28
For Earth – Best Connection is 45-60 degree west
Energetic proton fluxes
elevated for >12 hours
SDO AIA 131 Å
GOES-13
01:55 UT
Notes: Not only were the >10 Mev channel elevated well above our threshold, but the >50 and >100 channels as well, which tell us that this event was very efficient at accelerating the highest energy particles.

## Slide 29
Ground Level Enhancement
A subset of SEP events, a GLE event occurs when extremely high energy protons (>500 MeV/nuc) penetrate the Earth’s atmosphere. Collisions with atoms generate secondary particles that are measured at neutron monitoring (NM) stations on the ground.
NM Stations (http://www.nmdb.eu)
Neutron Monitoring Station in Oulu, Finland
Background ~105
Enhancement to ~125
Notes: The most extreme events…
This suspicious was confirmed by the detection of neutron enhancement at 4 stations. Those neutrons are reaction particles from relativistic protons
Add arrows to mark stations that observed May 17 GLE – what WAS THE TIME????
Save discussion of GLE events in SC 23 and characteristics of GLEs until 2nd half of talk. First half should only be observations!

## Slide 30
What causes strongest SEP events?
Or, how do the drivers relate to the SEP Flux?
Difficult to distinguish GLE from traditional SEP events:
Complexity of Active Region (AR)
  Most young, more compact
Magnetic connectivity of AR
  About ~50% are well connected
Magnitude of flare
  Average X3.8, but as low as M7.1
  Long duration
Magnitude of CME
  Range of speeds (~2,000 km/s average, but four events <1,500 km/s)
Seed particles
  Known to have harder spectrum
Sol
Nitta et al. 2012
CME-driven shocks are thought to play important role in low (<3Rs) corona
- Only imaged in mid-high corona (Ontiveros & Vourlidas 2009)
- Type II radio bursts
- Multiple CME events – doesn’t apply for May 17 event
Gopalswamy et al. 2012, Li et al. 2012, Mewaldt et al. 2012
Notes: Like I said, these events prompt more questions and more questions, so we want to look at all of the extreme events (GLE) and see if any characteristics of the solar part of the storm can tell us about what is happening. And the answer is that while there are trends, it’s not true that strong flare cause GLEs, as you saw only M5 cause the May event, it’s not the fastest and biggest CMEs.
Again I want to emphasize that these are all just speculations because most of the interesting stuff is happening in a region that is not well covered by coronagraphs.
End with: And so we are motivated to model the acceleration of particles by CME driven shocks in the low corona…
Comparing to previous AR1476 flares: Longer duration, but similar magnitude
March 7th event: flare and CME weaker, SEPs at Earth 20x weaker
Solar Cycle 23 GLE events: no CME in previous 24 hours (to generate seed particles)
What was special about this flare and CME to generate a GLE?
Timing: CME erupted during rise time of flare
Connectivity: AR well connected to Earth
CME speed 1,500 km/s sufficient to drive shock in low corona (Evans et al. 2008)
Must have been very wide CME (to impact STEREO A and Earth)
As is common, they were not geoeffective (Kp max =4)
Possible Type II radio burst indicates CME driven shock

## Slide 31
Exceptions to every rule!
September 28, 2012 – whole heliosphere event – C3.7 flare

## Slide 32
Where are NASA assets now?
The estimated speed, width and position were in a coupled coronal-heliospheric model to determine the path of the CME. WSA, an empirical model driven by photospheric magnetic field measurements, is used to drive 3D time dependent MHD model ENLIL. Simulations are performed at the CCMC
Mars and Earth are aligned!
Share a similar magnetic connectivity
We may lose real-time SEP
at STEREOs
Notes: Explain the figure set up.
Say that right now, Mercury, Mars and STEREO B are somewhat aligned, so a strong event from the eastern limb of the Sun would likely flood that area.

## Slide 33
Orientation
East 90
West 90
Earth

## Slide 34
GOES >10 MeV
13-100 MeV STEREO B
13-100 MeV STEREO A
GOES x-ray
M2.0
VCME=1540 km/s
X1.1
VCME=1360 km/s
X5.4/2200 km/s
X1.3/1800 km/s
M6.3/CME=1125 km/s
M8.4
VCME=1500 km/s
M7.9
VCME=2100 km/s
SEP: proton radiation
Both the CME(s) and flare(s) contribute to the SEP enhancement

## Slide 35
http://bit.ly/alert_SEP_layout
SEP Layout

## Slide 36: Summary
Our goal is to understand extreme energetic particle events
We use a new solar wind model driven by Alfvén waves coupled to a kinetic model of particle acceleration and transport, acting on observed quiet time particle spectra (scaled back to the corona)
We find strong acceleration
Acceleration can vary wildly from different regions of the CME due to interaction with structures in the corona, so using a single CME speed as a hard predictor of particle acceleration will not work
Is it more about the magnetic connectivity of the observer than the properties of the CMEs and flares?
  2012 May 17 GLE event suggests it could be
The events from Solar Cycle 24 provide interesting cases to test our model – can we explain the May 17 and July 23 observations?