## Slide 1: Space Weather impacts on satellites at different orbits
Outline
Intro of man-made satellites
Orbits
Different types of SWx effects on satellites
Satellite anomalies from the recent March 2012 SWx events
Yihua Zheng
June, 2015
Acknowledge: Mike Xapsos
Notes: Growing reliance on space technology

## Slide 2: 1st Satellite Launched Into Space
The world's first artificial satellite, the Sputnik 1, was launched by the Soviet Union in 1957.
4 October, 1957
marking the start of the Space Age
International Geophysical Year: 1957

## Slide 3: Space dog - Laika
the occupant of the Soviet spacecraft Sputnik 2 that was launched into outer space on November 3, 1957
Paving the way for human missions

## Slide 4: Explorer I – 1st U.S. Satellite
Explorer 1, was launched into Earth's orbit on a Jupiter C missile from Cape Canaveral, Florida, on January 31, 1958 - Inner belt

## Slide 5: Discovery of the Outer Van Allen RB
Pioneer 3 (launched 6 December 1958) and Explorer IV (launched July 26, 1958) both carried instruments designed and built by Dr. Van Allen. These spacecraft provided Van Allen additional data that led to discovery of a second radiation belt

## Slide 6: RBSP – more than half-century later

## Slide 7: Orbits

## Slide 8: Orbits
GEO
Yellow: MEO
Green-dash-dotted line: GPS
Cyan: LEO
Red dotted line: ISS

## Slide 9: Orbits
Different observing assets in near-Earth environment

## Slide 10: Orbits
A low Earth orbit (LEO) is generally defined as an orbit below an altitude of 2,000 km. Given the rapid orbital decay of objects below approximately 200 km, the commonly accepted definition for LEO is between 160–2,000 km (100–1,240 miles) above the Earth's surface.
Medium Earth orbit (MEO), sometimes called intermediate circular orbit (ICO), is the region of space around the Earth above low Earth orbit (altitude of 2,000 kilometres (1,243 mi)) and below geostationary orbit (altitude of 35,786 km (22,236 mi)).

## Slide 11: Orbit classification based on inclination
Inclined orbit: An orbit whose inclination in reference to the equatorial plane is not zero degrees.
  Polar orbit: An orbit that passes above or nearly above both poles of the planet on each revolution. Therefore it has an inclination of (or very close to) 90 degrees.
  Polar sun synchronous orbit: A nearly polar orbit that passes the equator at the same local time on every pass. Useful for image taking satellites because shadows will be nearly the same on every pass.
DMSP satellites

## Slide 12: GTO
A geosynchronous transfer orbit or geostationary transfer orbit (GTO) is a Hohmann transfer orbit used to reach geosynchronous or geostationary orbit.[1] It is a highly elliptical Earth orbit with apogee of 42,164 km (26,199 mi).[2] (geostationary (GEO) altitude, 35,786 km (22,000 mi) above sea level) and an argument of perigee such that apogee occurs on or near the equator. Perigee can be anywhere above the atmosphere, but is usually limited to only a few hundred km above the Earth's surface to reduce launcher delta-v (V) requirements and to limit the orbital lifetime of the spent booster.
SDO
The rapid cadence and continuous coverage required for SDO observations led to placing the satellite into an inclined geosynchronous orbit
Notes: http://solar-center.stanford.edu/sdo/
The rapid cadence and continuous coverage required for SDO observations led to placing the satellite into an inclined geosynchronous orbit. This allows for a nearly-continuous, high-data-rate, contact with a single, dedicated, ground station.
Nearly continuous observations of the Sun can be obtained from other orbits, such as low Earth orbit (LEO). If SDO were placed into an LEO it would be necessary to store large volumes of scientific data onboard until a downlink opportunity. The large data rate of SDO, along with the difficulties in managing a large on-board storage system, resulted in a requirement of continuous contact.
The disadvantges of this orbit include higher launch and orbit acquisition costs (relative to LEO) and eclipse (Earth shadow) seasons twice annually, During these 2-3 week eclipse periods, SDO will experience a daily interruption of solar observations. There will also be three lunar shadow events each year from this orbit.
This orbit is located on the outer reaches of the Earth's radiation belt where the radiation dose can be quite high. Additional shielding was added to the instruments and electronics to reduce the problems caused by exposure to radiation. Because this a Space Weather effect, SDO is affected by the very processes it is designed to study!

## Slide 13: Van Allen Probes
Two Spacecraft In an Elliptical Orbit

## Slide 14: MMS (Magnetospheric Multiscale Mission)
Notes: http://mms.space.swri.edu/mission-2.html

## Slide 15: Other types of orbits
Heliocentric orbit: An orbit around the Sun.
STEREO A and STEREO B
Interplanetary space
At different planets

## Slide 16: Orbit/Mission Design
New Horizon to Pluto
http://www.jhu.edu/jhumag/1105web/pluto.html
Dr. Yanping Guo, a mission design specialist at APL
Reduce the journey by three years
Closest approach to Pluto: 7:49:57 a.m. EDT (11:49:57 UTC) on July 14, 2015
For more information about New Horizon
http://www.nasa.gov/mission_pages/newhorizons/main/index.html

## Slide 17: Importance & Our Increasing Reliance on Space Systems
Scientific Research
  Space science
  Earth science
  Human exploration of space
  Aeronautics and space transportation
Navigation
Telecommunications
Defense
Space environment monitoring
Terrestrial weather monitoring
Courtesy: J. A. Pellish

## Slide 18: Space Weather impacts on spacecraft operation

## Slide 19: Space Environment Model Use in Mission Life Cycle
Mission Concept
Mission Planning
Design
Launch
Operations
Anomaly Resolution
Space Climate
Minimize Risk
Space Weather
Manage Residual Risk
Both
+
in situ
measurements
NASA Space Weather services

## Slide 20: Space Environment & Effects (1)
Mechanism | Effect | Source
Total Ionizing Dose (TID) | Degradation of microelectronics | Trapped protons Trapped electrons Solar protons
Displacement Damage Dose (DDD) | Degradation of optical components and some electronics Degradation of solar cells | Trapped protons Trapped electrons Solar protons Neutrons
Single-Event Effects (SEE) | Data corruption Noise on images System shutdowns Electronic component damage | GCR heavy ions Solar protons and heavy ions Trapped protons Neutrons
Surface Erosion | Degradation of thermal, electrical, optical properties Degradation of structural integrity | Particle radiation Ultraviolet Atomic oxygen Micrometeoroids Contamination

## Slide 21: Space Environment & Effects (2)
Mechanism | Effect | Source
Surface Charging | Biasing of instrument readings Power drains Physical damage | Dense, cold plasma Hot plasma
Deep Dielectric Charging | Biasing of instrument readings Electrical discharges causing physical damage | High-energy electrons
Structure Impacts | Structural damage Decompression | Micrometeoroids Orbital debris
Drag | Torques Orbital decay | Neutral thermosphere
UNCLASSIFIED

## Slide 22: Visual representation of space environment hazards

## Slide 23: Total Dose Effects
Total Ionizing Dose (TID) – cumulative damage resulting from ionization (electron-hole pair formation) causing
  Threshold voltage shifts
  Timing skews
  Leakage currents
Displacement Damage Dose (DDD) – cumulative damage resulting from displacement of atoms in semiconductor lattice structure causing:
  Carrier lifetime shortening
  Mobility degradation
0
2
4
6
8
10
12
14
0
2
4
6
8
10
Total Dose [krad(Si)]
Voltage During Erase Function
Failed to erase
Solar Array Degradation
128 Mb Samsung Flash Memory
DDD can also be referred to in the context of
Non-Ionizing Energy Loss (NIEL)
CREDIT: NRL & JPL
Messenger, S. R., Summers, G. P., Burke, E. A., Walters, R. J. and Xapsos, M. A. (2001), Modeling solar cell degradation in space: A comparison of the NRL displacement damage dose and the JPL equivalent fluence approaches. Prog. Photovolt: Res. Appl., 9: 103–121. doi: 10.1002/pip.357
Notes: Messenger, S. R., Summers, G. P., Burke, E. A., Walters, R. J. and Xapsos, M. A. (2001), Modeling solar cell degradation in space: A comparison of the NRL displacement damage dose and the JPL equivalent fluence approaches. Prog. Photovolt: Res. Appl., 9: 103–121. doi: 10.1002/pip.357

## Slide 24: Seven types SWx impacts for NASA’s robotic missions
Spacecraft surface charging caused by low-energy (< 100 keV) electrons, which are abundant, for example, in the inner magnetosphere during magnetospheric substorms.
Spacecraft internal electrostatic discharge caused by high-energy electrons (> 100 keV) that exist, for example, in the dynamic outer radiation belt of the Earth.
Single event effects due to high-energy (> 10 MeV) protons and heavier ions generated, for example, in solar flares and in coronal mass ejection (CME) shock fronts.
Total dosage effects caused by cumulative charged particle radiation received by spacecraft.
Increased spacecraft drag caused by the thermal expansion of the Earth’s upper atmosphere during space weather storms.
Communication disruptions between ground stations and spacecraft due to ionospheric irregularities
Attitude control disruptions caused, for example, by large storm-time magnetic field fluctuations in the geostationary orbit.
Feedback from our annual SWx workshop for robotic missions

## Slide 25: Space weather impacts on sc (cont’d)
low-energy protons (< 10 MeV) pose a problem due to trapping into charge-coupled device (CCD) substrates.
 virtually any part of electron and ion spectra ranging from low to relativistic energies can impact spacecraft operations.

## Slide 26: Space Environment Anomalies
According to a study by the Aerospace Corporation the 2 most common types of spacecraft anomalies by far are due to electrostatic discharge (ESD) and single event effects (SEE)
Reported results*:
Anomaly Type: | Number of Occurrences:
ESD | 162
SEE | 85
Total Dose and Damage | 16
Miscellaneous | 36
* H.C. Koons et al., 6th Spacecraft Technology Conference, AFRL-VS-TR-20001578, Sept. 2000

## Slide 27: Surface charging: which can lead to electrostatic discharges (ESD), ESD: can lead to a variety of problems, including component failure and phantom commands in spacecraft electronics [Purvis et al., 1984].
Purvis, C. K., H. B. Garrett, A. C. Wittlesey, and N. J. Stevens (1984),
Design guidelines for assessing and controlling spacecraft charging
effects, NASA Tech. Pap. 2361
https://standards.nasa.gov/documents/detail/3314877
Surface Charging

## Slide 28: Surface Charging
Commercial satellite anomaly
More often in the midnight to morning sector
<100 keV e- distribution: similar behavior as spacecraft anomalies
=> Surface charging might be the main cause of the anomalies.
Choi, H.‐S., J. Lee, K.‐S. Cho, Y.‐S. Kwak, I.‐H. Cho, Y.‐D. Park, Y.‐H. Kim, D. N. Baker, G. D. Reeves, and D.‐K. Lee (2011), Analysis of GEO spacecraft anomalies: Space weather relationships, Space Weather, 9, S06001,doi:10.1029/2010SW000597.
Substorm injections ( Aurora)

## Slide 29
Surface Charging Hazards distribution

## Slide 30: NASA Document on Mitigating Charging Effects
Title: Mitigating In-Space Charging Effects-A Guideline
Document Date: 2011-03-03
Revalid and Reaffirmed Date: 2016-03-03
Revision: A
Organization: NASA

## Slide 31
Ring current model data show same
Galaxy 15 failure on April 5, 2010
- surface charging might play a role
22keV electrons 4/5, 8:16-9:32Z
Galaxy 15 failed approx 9:48Z

## Slide 32: Environmental Source of SEEs
Single Event Environments in Space
  Galactic Cosmic Rays
  Solar Particle Events (flare/CME)
  Trapped Protons in the inner belt (1 – 3 RE)
  High energy neutrons

## Slide 33: SEE source in Space
Solar Particle
Events (flare/CME)
Trapped
Particles (SAA)
Galactic
Cosmic Rays
High Energy
Particle
Radiation
Most unpredictable

## Slide 34: Galactic Cosmic Rays
Galactic cosmic rays (GCR) are high-energy charged particles that originate outside our solar system.
Supernova explosions are a significant source
Anticorrelation with solar activity
More pronounced/intense during solar minimum

## Slide 35: South Atlantic Anomaly
Dominates the radiation environment for altitudes less than about 1000 km.
Caused by tilt and shift of geomagnetic axis relative to rotational axis.
Inner edge of proton belt is at lower altitudes south and east of Brazil.
E.J. Daly et al., IEEE TNS, April 1996

## Slide 36: South Atlantic Anomaly
From SPENVIS, http://www.spenvis.oma.be/
Solar Maximum

## Slide 37: Solar Particle Events
Caused by flare/CME

## Slide 38: Characteristics of SEPs
Elemental composition* (may vary event by event)
  96.4% protons
  3.5% alpha particles
  0.1% heavier ions (not to be neglected!)
Energies: up to ~ GeV/nucleon
Event magnitudes:
  > 10 MeV/nucleon integral fluence: can exceed 109 cm-2
  > 10 MeV/nucleon peak flux: can exceed 105 cm-2s-1

## Slide 39: Solar Cycle Dependence
Most unpredictable

## Slide 40: What is a Single Event Effect?
Single Event Effect (SEE) – any measureable effect in a circuit caused by single incident ion
  Non-destructive – SEU (Single Event Upset), SET (single event transients), MBU (Multiple Bit Upsets), SHE (single-event hard error)
  Destructive – SEL (single event latchup), SEGR (single event gate rupture), SEB (single event burnout)
Destructive event
in a COTS 120V
DC-DC Converter

## Slide 41: Single Event Upsets
SEUs: are soft errors, and non-destructive. They normally appear as transient pulses in logic or support circuitry, or as bitflips in memory cells or registers.

## Slide 42: Destructive SEEs
Several types of hard errors, potentially destructive, can appear:
Single Event Latchup (SEL) results in a high operating current, above device specifications, and must be cleared by a power reset.
Other hard errors include Burnout of power MOSFETS (Metal Oxide Semiconductor Field-Effect Transistor) , Gate Rupture, frozen bits, and noise in CCDs.

## Slide 43: Anomalies March 2012 SWx events SEEs dominate
Quite a few NASA spacecraft experienced anomalies, majority of which are SEEs. Some of them required reset/reboot.
Details to be discussed later.

## Slide 44
Internal Charging
- energetic electrons in the outer radiation belt
CIR HSS geomagnetic storm
CME geomagnetic storms

## Slide 45: Space Environment Hazards (different types of charging) for Spacecraft in the near-Earth environment
Van Allen Probes
0
200
400
600
HEO-2 Charging Events
L ~ Equatorial Radial Distance (RE)
HEO
GPS
GEO
0
50
100
150
200
250
CRRES MEP-SEU Anomalies
0
CRRES VTCW Anomalies
Inner
Belt
Slot
Outer Belt
5
10
15
1
2
3
4
5
6
7
8
SEUs
Internal
Charging
Surface
Charging
(Dose behind 82.5 mils Al)
Single Event Effects tend to occur in the inner (proton) belt and at higher L shells when a solar particle event is in progress.
Internal electrostatic discharges (ESD) occur over a broad range of L values corresponding to the outer belt, where penetrating electron fluxes are high (300 keV – few MeV electrons)
Surface ESD tends to occur when the spacecraft or surface potential is elevated: at 2000-0800 local time in the plasma sheet and in regions of intense field-aligned currents (auroral zone) (few eV – 50 keV) - plasma sheet, ring current, aurora zone, magnetosheath
Event Total Dose occurs primarily in orbits that rarely see trapped protons in the 1-20 MeV range (e.g., GEO, GPS) because these are the orbits for which solar particle events and transient belts make up a majority of the proton dose (including displacement damage)
Plasma Sheet
Courtesy: Paul O’Brien

## Slide 46: Human Safety in Space
GCR
SEP
Johnson Space Center/Space Radiation Analysis Group (SRAG)
Limit: the > 100 MeV flux exceeding 1pfu
(1 pfu = 1 particle flux unit= 1/cm^2/sec/sr)
All clear (EVA –extravehicular activity)

## Slide 47: Operator response to SWx impacts spacecraft specific/instrument specific

## Slide 48
March 7 flares/CMEs

## Slide 49
GOES >10 MeV
13-100 MeV STEREO B
13-100 MeV STEREO A
GOES x-ray
M2.0
VCME=1540 km/s
X1.1
VCME=1360 km/s
X5.4/2200 km/s
X1.3/1800 km/s
M6.3/CME=1125 km/s
M8.4
VCME=1500 km/s
M7.9
VCME=2100 km/s
SEP: proton radiation (flare and CME)

## Slide 50: Major events from the long-lasting AR1429 during March 4 – 28, 2012

## Slide 51
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
Flares of the Major Earth-Facing Events viewed by SDO EVE (x-ray)

## Slide 52
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
Flares of the Major Earth-Facing Events viewed by SDO AIA 131

## Slide 53
Orientation
East 90
West 90
Earth

## Slide 54
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
The Corresponding CMEs Associated with the Flares

## Slide 55
STA: 2012-03-18
STA: 2012-03-21
STB: 2012-03-24
STB: 2012-03-26
Backsided events in STEREO EUVI 195A (top) and CME model simulations (bottom)

## Slide 56
2012-03-26 23:12UT
VCME=1500 km/s
13-100 MeV STEREO B
13-100 MeV STEREO A
2012-03-18 00:39UT
VCME=1450 km/s
2012-03-21 07:39 UT
VCME=1550 km/s
2012-03-24 00:39UT
VCME=1600 km/s
Enhanced proton radiation at STEREO A and B from the backsided events.
Notes: Enhanced proton radiation at STEREO A and B from the backsided events.

## Slide 57: Space Weather (all in one)
Space weather drivers
Outside the solar system
GCRs (Galactic Cosmic Rays)
Solar flares
CMEs
Coronal Hole High Speed solar wind Streams (HSS)
Sun
Radiation storms
Geomagnetic storms
Ionospheric storms
Radio blackout storms
SPEs
(Solar energetic Particle Events)
Dynamic Radiation Belts Environment
Types of Storms
Drivers and Storms

## Slide 58
Radiation Storms
Geomagnetic Storms
Ionospheric Storms
Radio Blackouts due to flares
Storms and Effects
Radiation hazards to humans
SEEs on spacecraft components and electronics
PCA on radio waves
Energetic ions
Energetic electrons
Internal charging of electronics
Large/rapid variations/disturbances in space and time (in fields and plasma/neutral distribution)
Enhancement in currents
Affect communication
Navigation
Surface charging
Radio wave propagation
Radio emissions/noise associated with flares (direct impacts)
X-ray/EUV emission altering ionospheric structure/composition (indirect)
Radio wave blackouts
(dayside ionosphere)

## Slide 59: Supplementary Material/contact info
View our video, Incredible Active Region 1429: One for the record books, to learn more about the activities from this region from March 4 – March 28, 2012. http://youtu.be/PbyJswbX4VA
This video has been updated at the following link: http://youtu.be/dxl5drPY8xQ (And also available on http://vimeo.com/nasaswc/ar1429)
Summary Video of the March 7, 2012 event
    http://youtu.be/HeoKf6NfEJI
    Full text of event summary
    http://goo.gl/dTnfd
http://swc.gsfc.nasa.gov/main/
NASA Space Weather Center

## Slide 60: Supplementary material
Youtube video from Henry Garrett at JPL - http://www.youtube.com/watch?v=NarzGDuYYX4
2 hour and 40 minutes long

## Slide 61: SWx Services provided by NASA/SWC