## Slide 1: Space Weather impacts on satellites
Outline
Intro of man-made satellites
Orbits
Different types of space weather effects on satellites
Satellite anomalies from the Oct 2003 and the March 2012 SWx events
Yihua Zheng
June 8, 2017
Acknowledge:
Mike Xapsos
Joe Minow
Notes: Growing reliance on space technology

## Slide 2: 1st Satellite Launched Into Space
The world's first artificial satellite, the Sputnik 1, was launched by the Soviet Union in 1957.
4 October, 1957
marking the start of the Space Age
International Geophysical Year: 1957

## Slide 3: Space dog - Laika
the occupant of the Soviet spacecraft Sputnik 2 that was launched into outer space on November 3, 1957
Paving the way for human missions

## Slide 4: Explorer I – 1st U.S. Satellite
Explorer 1, was launched into Earth's orbit on a Jupiter C missile from Cape Canaveral, Florida, on January 31, 1958 - Inner belt

## Slide 5: Discovery of the Outer Van Allen RB
Pioneer 3 (launched 6 December 1958) and Explorer IV (launched July 26, 1958) both carried instruments designed and built by Dr. Van Allen. These spacecraft provided Van Allen additional data that led to discovery of a second radiation belt

## Slide 6: Orbits

## Slide 7: Orbits
GEO
Yellow: MEO
Green-dash-dotted line: GPS
Cyan: LEO
Red dotted line: ISS

## Slide 8: Orbits
Different observing assets in near-Earth environment

## Slide 9: Orbits
A low Earth orbit (LEO) is generally defined as an orbit below an altitude of 2,000 km. Given the rapid orbital decay of objects below approximately 200 km, the commonly accepted definition for LEO is between 160–2,000 km (100–1,240 miles) above the Earth's surface.
Medium Earth orbit (MEO), sometimes called intermediate circular orbit (ICO), is the region of space around the Earth above low Earth orbit (altitude of 2,000 kilometres (1,243 mi)) and below geostationary orbit (altitude of 35,786 km (22,236 mi)).

## Slide 10: Orbit classification based on inclination
Inclined orbit: An orbit whose inclination in reference to the equatorial plane is not zero degrees.
  Polar orbit: An orbit that passes above or nearly above both poles of the planet on each revolution. Therefore it has an inclination of (or very close to) 90 degrees.
  Polar sun synchronous orbit: A nearly polar orbit that passes the equator at the same local time on every pass. Useful for image taking satellites because shadows will be nearly the same on every pass.
DMSP satellites

## Slide 11: Van Allen Probes
Two Spacecraft In an Elliptical Orbit

## Slide 12: ERG/Arase
Orbit info
  Altitude
    Perigee about 440 km, Apogee: about 32,000 km
  Inclination
    32 degrees
  Elliptical orbit
  Period: 570 min
Notes: ERG: exploration of Energization and Radiation in Geospace.

## Slide 13: MMS (Magnetospheric Multiscale Mission)
Notes: http://mms.space.swri.edu/mission-2.html

## Slide 14: Other types of orbits
Heliocentric orbit: An orbit around the Sun.
STEREO A and STEREO B
Interplanetary space
At different planets

## Slide 15: Orbit/Mission Design
New Horizon to Pluto
http://www.jhu.edu/jhumag/1105web/pluto.html
Dr. Yanping Guo, a mission design specialist at APL
Reduce the journey by three years
Closest approach to Pluto: 7:49:57 a.m. EDT (11:49:57 UTC) on July 14, 2015
For more information about New Horizon
http://www.nasa.gov/mission_pages/newhorizons/main/index.html

## Slide 16: Importance & Our Increasing Reliance on Space Systems
Scientific Research
  Space science
  Earth science
  Human exploration of space
  Aeronautics and space transportation
Navigation
Telecommunications
Defense
Space environment monitoring
Terrestrial weather monitoring
Courtesy: J. A. Pellish

## Slide 17: Space Weather and Spacecraft Operations
The primary approach for the spacecraft industry to mitigate the effects of space weather is to design satellites to operate under extreme environmental conditions to the maximum extent possible within cost and resource constraints
  “Severe Space Weather Events--Understanding Societal and Economic Impacts Workshop Report,”
  National Academies Press, Washington, DC, 2008 http://www.nap.edu/catalog/12507.html
This technique is rarely 100% successful and space weather will typically end up impacting some aspect of a space mission
  Some space weather issues are common to all spacecraft, e.g., space situational awareness is one example
  Specific details of space weather interactions with a spacecraft are often unique because spacecraft systems are unique, there is no “standard” space weather support to mission operations

## Slide 18: Space Weather impacts on spacecraft operation

## Slide 19: Space Environment Model Use in Mission Life Cycle
Mission Concept
Mission Planning
Design
Launch
Operations
Anomaly Resolution
Space Climatology
Minimize Risk
Space Weather
Manage Residual Risk
Both
+
in situ
measurements
NASA Space Weather services

## Slide 20: Space Climatology and Space Weather
Space Climatology:
  Variability over months to years
  Space environment effects on both satellites and launch vehicles are best mitigated by good design
Space Weather
  Variability over minutes to days
  Effects mitigated by design or operational controls
  Design satellites to withstand mean, extreme space weather events that may occur during time on orbit

## Slide 21: Space Environment & Effects (1)
Mechanism | Effect | Source
Total Ionizing Dose (TID) | Degradation of microelectronics | Trapped protons Trapped electrons Solar protons
Displacement Damage Dose (DDD) | Degradation of optical components and some electronics Degradation of solar cells | Trapped protons Trapped electrons Solar protons Neutrons
Single-Event Effects (SEE) | Data corruption Noise on images System shutdowns Electronic component damage | GCR heavy ions Solar protons and heavy ions Trapped protons Neutrons
Surface Erosion | Degradation of thermal, electrical, optical properties Degradation of structural integrity | Particle radiation Ultraviolet Atomic oxygen Micrometeoroids Contamination

## Slide 22: Space Environment & Effects (2)
Mechanism | Effect | Source
Surface Charging | Biasing of instrument readings Power drains Physical damage | Dense, cold plasma Hot plasma (ring current, aurora population) (few eV to 10s keV)
Deep Dielectric Charging | Biasing of instrument readings Electrical discharges causing physical damage | High-energy electrons (>300 keV)
Structure Impacts | Structural damage Decompression | Micrometeoroids Orbital debris
Satellite Drag | Torques Orbital decay | Neutral thermosphere
UNCLASSIFIED

## Slide 23: Space Environment & Effects
Total Ionizing Dose (TID)
Degradation of microelectronics
Displacement Damage Dose (DDD)
Trapped protons, Trapped electrons, Solar protons, Neutrons
Degradation of optical components and some electronics
Single-Event Effects (SEE)
GCR heavy ions, Solar protons and heavy ions, Trapped protons, Neutrons
Data corruption
Surface Erosion
Degradation of thermal, electrical, optical properties
Degradation of solar cells
Trapped protons, Trapped electrons, Solar protons
Noise on images
System shutdowns
Electronic component damage
Particle radiation, Ultraviolet, Atomic oxygen, Micrometeoroids, Contamination
Degradation of structural integrity
Surface Charging
Dense, cold plasma, Hot plasma
Biasing of instrument readings
Power drains
Physical damage
Deep Dielectric Charging
High-energy electrons
Biasing of instrument readings
Electrical discharges causing
physical damage
Structure Impacts
Micrometeoroids, Orbital debris
Structural damage
Decompression
Satellite Drag
Neutral thermosphere
Torques
Orbital decay

## Slide 25: Visual representation of space environment hazards

## Slide 26: Space Environment Effects
McKnight 2015

## Slide 27: Space Environment Anomalies
According to a study by the Aerospace Corporation the 2 most common types of spacecraft anomalies by far are due to electrostatic discharge (ESD) and single event effects (SEE)
Reported results*:
Anomaly Type: | Number of Occurrences:
ESD | 162
SEE | 85
Total Dose and Damage | 16
Miscellaneous | 36
* H.C. Koons et al., 6th Spacecraft Technology Conference, AFRL-VS-TR-20001578, Sept. 2000

## Slide 28: 2003 Halloween Storm Impacts on Spacecraft (3)
Oct 28-31:
  CDS instrument on SOHOspacecraft at L1 commanded into safe mode for 3 days
  Mars Odyssey spacecraft entered safe mode, MARIE instrument had a temperature red alarm leading it to be powered off (Oct. 28). S/C memory error during downloading on 29 Oct corrected with a cold reboot on Oct. 31
  Both Mars Explorer Rover spacecraft entered “sun idle” mode due to excessive start tracker events
Oct 29:
  NASA’s Earth Sciences Mission Office directed all instruments on 5 spacecraft be turned off or safed due to Level 5 storm prediction. Satellites affected include AQUA, Landsat, TERRA, TOMS, and TRMM
Oct 30:
  ACE & Wind solar wind satellites lost plasma observations
  Electron sensors of GOESsatellite in geosynchronous orbit saturated
Nov 2:
  Chandra observations halted again autonomously due to radiation. Resumption of observations delayed for days
Nov. 6:
  Polar TIDE instrument reset itself and high voltage supplies were disabled; recovered within 24 hr.
  Mars Odyssey spacecraft commanded out of Safe mode; operations nominal.
adapted from Allen and Wilkerson, 2010
http://www.ngdc.noaa.gov/stp/satellite/anomaly/2010_sctc/docs/1-1_JAllen.pdf

## Slide 29: Seven types SWx impacts for NASA’s robotic missions
Spacecraft surface charging caused by low-energy (< 100 keV) electrons, which are abundant, for example, in the inner magnetosphere during magnetospheric substorms.
Spacecraft internal electrostatic discharge caused by high-energy electrons (> 100 keV) that exist, for example, in the dynamic outer radiation belt of the Earth.
Single event effects due to high-energy (> 10 MeV) protons and heavier ions generated, for example, in solar flares and in coronal mass ejection (CME) shock fronts.
Total dosage effects caused by cumulative charged particle radiation received by spacecraft.
Increased spacecraft drag caused by the thermal expansion of the Earth’s upper atmosphere during space weather storms.
Communication disruptions between ground stations and spacecraft due to ionospheric irregularities
Attitude control disruptions caused, for example, by large storm-time magnetic field fluctuations in the geostationary orbit.
Feedback from our annual SWx workshop for robotic missions

## Slide 30: Space weather impacts on sc (cont’d)
low-energy protons (< 10 MeV) pose a problem due to trapping into charge-coupled device (CCD) substrates.
 virtually any part of electron and ion spectra ranging from low to relativistic energies can impact spacecraft operations.

## Slide 31: A few types of space weather impacts on spacecraft impacts

## Slide 32: Surface charging: which can lead to electrostatic discharges (ESD), ESD: can lead to a variety of problems, including component failure and phantom commands in spacecraft electronics [Purvis et al., 1984].
Purvis, C. K., H. B. Garrett, A. C. Wittlesey, and N. J. Stevens (1984),
Design guidelines for assessing and controlling spacecraft charging
effects, NASA Tech. Pap. 2361
https://standards.nasa.gov/documents/detail/3314877
Surface Charging

## Slide 33: Surface Charging
Commercial satellite anomaly
More often in the midnight to morning sector
<100 keV e- distribution: similar behavior as spacecraft anomalies
=> Surface charging might be the main cause of the anomalies.
Choi, H.‐S., J. Lee, K.‐S. Cho, Y.‐S. Kwak, I.‐H. Cho, Y.‐D. Park, Y.‐H. Kim, D. N. Baker, G. D. Reeves, and D.‐K. Lee (2011), Analysis of GEO spacecraft anomalies: Space weather relationships, Space Weather, 9, S06001,doi:10.1029/2010SW000597.
Substorm injections ( Aurora)

## Slide 34
Surface Charging Hazards distribution

## Slide 35: NASA Document on Mitigating Charging Effects
Title: Mitigating In-Space Charging Effects-A Guideline
Document Date: 2011-03-03
Revalid and Reaffirmed Date: 2016-03-03
Revision: A
Organization: NASA

## Slide 36
Ring current model data show same
Galaxy 15 failure on April 5, 2010
- surface charging might play a role
22keV electrons 4/5, 8:16-9:32Z
Galaxy 15 failed approx 9:48Z

## Slide 37: Environmental Source of Single Event Effects
Single Event Environments in Space
  Galactic Cosmic Rays
  Solar Particle Events (flare/CME)
  Trapped Protons in the inner belt (1 – 3 RE)
  High energy neutrons

## Slide 38: SEE source in Space
Solar Particle
Events (flare/CME)
Trapped
Particles (SAA)
Galactic
Cosmic Rays
High Energy
Particle
Radiation
Most unpredictable
High energy neutrons

## Slide 39: Galactic Cosmic Rays
Galactic cosmic rays (GCR) are high-energy charged particles that originate outside our solar system.
Supernova explosions are a significant source
Anticorrelation with solar activity
More pronounced/intense during solar minimum

## Slide 40: South Atlantic Anomaly
Dominates the radiation environment for altitudes less than about 1000 km.
Caused by tilt and shift of geomagnetic axis relative to rotational axis.
Inner edge of proton belt is at lower altitudes south and east of Brazil.
E.J. Daly et al., IEEE TNS, April 1996

## Slide 41: South Atlantic Anomaly
From SPENVIS, http://www.spenvis.oma.be/
Solar Maximum

## Slide 42: Solar Particle Events
Caused by flare/CME

## Slide 43: Characteristics of SEPs
Elemental composition* (may vary event by event)
  96.4% protons
  3.5% alpha particles
  0.1% heavier ions (not to be neglected!)
Energies: up to ~ GeV/nucleon
Event magnitudes:
  > 10 MeV/nucleon integral fluence: can exceed 109 cm-2
  > 10 MeV/nucleon peak flux: can exceed 105 cm-2s-1

## Slide 44: Solar Cycle Dependence
Most unpredictable

## Slide 45: Single Event Effects (SEE)
Single event effect (SEE) : current generated by ion passing through the sensitive volume of a biased electronic device changes the device operating state
SEE Generated by Heavy Ions (Z=2-92)
High linear energy transfer (LET) rate of heavy ions produces ionization along track as ion slows down
Dense ionization track over a short range produces sufficient charge in sensitive volume to cause SEE
SEE is caused directly by ionization produced by incident heavy ion particles
SEE Generated by Protons (Z=1)
Proton LET is too low to generate SEE, but secondary heavy ions are produced in nuclear reactions with nuclei of atoms (usually silicon) inside electronics. Energy is transferred to a target atom fragment or recoil ion with high LET and charge deposited by recoil ion(s) is the direct cause of SEE.
Only a small fraction of protons are converted to such secondary particles (1 in 10^4 to 10^5).

## Slide 46: What is a Single Event Effect?
Single Event Effect (SEE) – any measureable effect in a circuit caused by single incident ion
  Non-destructive – SEU (Single Event Upset), SET (single event transients), MBU (Multiple Bit Upsets), SHE (single-event hard error)
  Destructive – SEL (single event latchup), SEGR (single event gate rupture), SEB (single event burnout)
Destructive event
in a COTS 120V
DC-DC Converter

## Slide 47: Single Event Upsets
SEUs: are soft errors, and non-destructive. They normally appear as transient pulses in logic or support circuitry, or as bitflips in memory cells or registers.

## Slide 48: Destructive SEEs
Several types of hard errors, potentially destructive, can appear:
Single Event Latchup (SEL) results in a high operating current, above device specifications, and must be cleared by a power reset.
Other hard errors include Burnout of power MOSFETS (Metal Oxide Semiconductor Field-Effect Transistor) , Gate Rupture, frozen bits, and noise in CCDs.

## Slide 49: Anomalies March 2012 SWx events SEEs dominate
Quite a few NASA spacecraft experienced anomalies, majority of which are SEEs. Some of them required reset/reboot.
Details to be discussed later.

## Slide 50
Internal Charging
- energetic electrons in the outer radiation belt
CIR HSS geomagnetic storm
CME geomagnetic storms

## Slide 51: Space Environment Hazards (different types of charging) for Spacecraft in the near-Earth environment
Van Allen Probes
0
200
400
600
HEO-2 Charging Events
L ~ Equatorial Radial Distance (RE)
HEO
GPS
GEO
0
50
100
150
200
250
CRRES MEP-SEU Anomalies
0
CRRES VTCW Anomalies
Inner
Belt
Slot
Outer Belt
5
10
15
1
2
3
4
5
6
7
8
SEUs
Internal
Charging
Surface
Charging
(Dose behind 82.5 mils Al)
Single Event Effects tend to occur in the inner (proton) belt and at higher L shells when a solar particle event is in progress.
Internal electrostatic discharges (ESD) occur over a broad range of L values corresponding to the outer belt, where penetrating electron fluxes are high (300 keV – few MeV electrons)
Surface ESD tends to occur when the spacecraft or surface potential is elevated: at 2000-0800 local time in the plasma sheet and in regions of intense field-aligned currents (auroral zone) (few eV – 50 keV) - plasma sheet, ring current, aurora zone, magnetosheath
Event Total Dose occurs primarily in orbits that rarely see trapped protons in the 1-20 MeV range (e.g., GEO, GPS) because these are the orbits for which solar particle events and transient belts make up a majority of the proton dose (including displacement damage)
Plasma Sheet
Courtesy: Paul O’Brien

## Slide 52: Total Dose Effects
Total Ionizing Dose (TID) – cumulative damage resulting from ionization (electron-hole pair formation) causing
  Threshold voltage shifts
  Timing skews
  Leakage currents
Displacement Damage Dose (DDD) – cumulative damage resulting from displacement of atoms in semiconductor lattice structure causing:
  Carrier lifetime shortening
  Mobility degradation
0
2
4
6
8
10
12
14
0
2
4
6
8
10
Total Dose [krad(Si)]
Voltage During Erase Function
Failed to erase
Solar Array Degradation
128 Mb Samsung Flash Memory
DDD can also be referred to in the context of
Non-Ionizing Energy Loss (NIEL)
CREDIT: NRL & JPL
Messenger, S. R., Summers, G. P., Burke, E. A., Walters, R. J. and Xapsos, M. A. (2001), Modeling solar cell degradation in space: A comparison of the NRL displacement damage dose and the JPL equivalent fluence approaches. Prog. Photovolt: Res. Appl., 9: 103–121. doi: 10.1002/pip.357
Notes: Messenger, S. R., Summers, G. P., Burke, E. A., Walters, R. J. and Xapsos, M. A. (2001), Modeling solar cell degradation in space: A comparison of the NRL displacement damage dose and the JPL equivalent fluence approaches. Prog. Photovolt: Res. Appl., 9: 103–121. doi: 10.1002/pip.357

## Slide 53: Human Safety in Space
GCR
SEP
Johnson Space Center/Space Radiation Analysis Group (SRAG)
Limit: the > 100 MeV flux exceeding 1pfu
(1 pfu = 1 particle flux unit= 1/cm^2/sec/sr)
All clear (EVA –extravehicular activity)

## Slide 54: Examples of space environment effects on satellites

## Slide 55: 2003 Halloween Storm Impacts on Spacecraft (1)
Oct 23:
  Genesis satellite at L1 entered safe mode, normal operations resumed on Nov. 3.
  Midori-2(ADEOS-2) Earth-observing satellite power system failed, safe mode, telemetry lost (23:55), spacecraft lost
Oct 24:
  Stardustcomet mission went into safe mode due to read errors; recovered.
  Chandra X-ray Observatory astronomy satellite observations halted due to high radiation levels (09:34EDT), restarted Oct. 25
  GOES-9, 10 and 12 had high bit error rates (9 and 10), magnetic torquers disabled due to geomagnetic activity
Oct 25:
  RHESSI solar satellite had spontaneous CPU reset (10:42)
Oct 26:
  SMART-1had auto shutdown of engine due to increased radiation level in lunar transfer orbit (19:23)
Oct 27:
  NOAA-17AMSU-A1 lost scanner
  GOES-8 X-ray sensor turned itself off and could not be recovered
Oct 28-30:
  Astronauts on Intl. Space Station went into service module for radiation protection
  Instrument on Integral satellite went into safe mode because of increased radiation
  Chandra observations halted again autonomously, resumed Nov 1

## Slide 56: Major indices during 2003 Dst, Kp, F10.7
DOY 296: Oct 23

## Slide 57: 2003 Halloween Storm Impacts on Spacecraft (2)
Oct 28:
  DMSP F16 SSIES sensor lost data twice, on Oct. 28 and Nov. 3; recovered. microwave sounder lost oscillator; switched to redundant system
  SIRTF, in orbit drifting behind Earth, turned off science experiments and went to Earth pointing due to high proton fluxes, 4 days of operations lost
  Microwave Anisotropy Probe spacecraft star tracker reset and backup tracker autonomously turned on, prime tracker recovered
Oct 29:
  Kodamadata relay satellite in GEO; safe mode, signals noisy, recovery unknown
  RHESSIsatellite had 2 more spontaneous resets of CPU (28, 17:40; 29, 03:32).
  CHIPS satellite computer went offline on Oct. 29 and contact lost with the spacecraft for 18 hr. When contacted the S/C was tumbling; recovered successfully. Offline for a total of 27 hrs.
  X-ray Timing Explorer science satellite Proportional Counter Assembly (PCA) experienced high voltages and the All Sky Monitor autonomously shut off, both instruments recovered Oct 30 but PCA again shut down. PCA recovery delayed into November.
Allen and Wilkerson, 2010
http://www.ngdc.noaa.gov/stp/satellite/anomaly/2010_sctc/docs/1-1_JAllen.pdf

## Slide 58: Space weather impacts on satellite positioning/tracking
After a large geomagnetic storm in March, 1989, the North American Aerospace Defense Command (NORAD) had to re-identify hundreds of objects due to loss of tracking and compute their new orbits. During the same March 1989 storm event, for example, the NASA's Solar Maximum Mission (SMM) spacecraft had dropped its altitude as if it hit a “brick wall" due to the increased atmospheric drag.
http://www.swpc.noaa.gov/impacts/satellite-drag

## Slide 59: Operator response to SWx impacts for the March 2012 events spacecraft specific/instrument specific

## Slide 60
March 7 flares/CMEs

## Slide 61
GOES >10 MeV
13-100 MeV STEREO B
13-100 MeV STEREO A
GOES x-ray
M2.0
VCME=1540 km/s
X1.1
VCME=1360 km/s
X5.4/2200 km/s
X1.3/1800 km/s
M6.3/CME=1125 km/s
M8.4
VCME=1500 km/s
M7.9
VCME=2100 km/s
SEP: proton radiation (flare and CME)

## Slide 62: Major events from the long-lasting AR1429 during March 4 – 28, 2012

## Slide 63
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
Flares of the Major Earth-Facing Events viewed by SDO EVE (x-ray)

## Slide 64
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
Flares of the Major Earth-Facing Events viewed by SDO AIA 131

## Slide 65
Orientation
East 90
West 90
Earth

## Slide 66
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
The Corresponding CMEs Associated with the Flares

## Slide 67
STA: 2012-03-18
STA: 2012-03-21
STB: 2012-03-24
STB: 2012-03-26
Backsided events in STEREO EUVI 195A (top) and CME model simulations (bottom)

## Slide 68
2012-03-26 23:12UT
VCME=1500 km/s
13-100 MeV STEREO B
13-100 MeV STEREO A
2012-03-18 00:39UT
VCME=1450 km/s
2012-03-21 07:39 UT
VCME=1550 km/s
2012-03-24 00:39UT
VCME=1600 km/s
Enhanced proton radiation at STEREO A and B from the backsided events.
Notes: Enhanced proton radiation at STEREO A and B from the backsided events.

## Slide 69: Space Weather (all in one)
Space weather drivers
Outside the solar system
GCRs (Galactic Cosmic Rays)
Solar flares
CMEs
Coronal Hole High Speed solar wind Streams (HSS)
Sun
Radiation storms
Geomagnetic storms
Ionospheric storms
Radio blackout storms
SPEs
(Solar energetic Particle Events)
Dynamic Radiation Belts Environment
Types of Storms
Drivers and Storms

## Slide 70
Radiation Storms
Geomagnetic Storms
Ionospheric Storms
Radio Blackouts due to flares
Storms and Effects
Radiation hazards to humans
SEEs on spacecraft components and electronics
PCA on radio waves
Event total dose
Energetic ions
Energetic electrons
Internal charging of electronics
Large/rapid variations/disturbances in space and time (in fields and plasma/neutral distribution)
Enhancement in currents
Affect
Communication
Navigation
Surface charging
Radio wave propagation
Radio emissions/noise associated with flares (direct impacts)
X-ray/EUV emission altering ionospheric structure/composition (indirect)
Radio wave blackouts
(dayside ionosphere)

## Slide 71: Supplementary Material/contact info
View our video, Incredible Active Region 1429: One for the record books, to learn more about the activities from this region from March 4 – March 28, 2012. http://youtu.be/PbyJswbX4VA
This video has been updated at the following link: http://youtu.be/dxl5drPY8xQ (And also available on http://vimeo.com/nasaswc/ar1429)
Summary Video of the March 7, 2012 event
    http://youtu.be/HeoKf6NfEJI
    Full text of event summary
    http://goo.gl/dTnfd
http://swc.gsfc.nasa.gov/main/
NASA Space Weather Center

## Slide 72: Supplementary material
Youtube video from Henry Garrett at JPL - http://www.youtube.com/watch?v=NarzGDuYYX4
2 hour and 40 minutes long

## Slide 73: SWx Services provided by NASA/SWC