## Slide 1: Space Weather impacts on satellites at different orbits
Outline
Intro of man-made satellites
Orbits
Different types of SWx effects on satellites
Satellite anomalies from the recent March 2012 SWx events
Yihua Zheng
Feb 25, 2015
Notes: Growing reliance on space technology

## Slide 2: 1st Satellite Launched Into Space
The world's first artificial satellite, the Sputnik 1, was launched by the Soviet Union in 1957.
4 October, 1957
marking the start of the Space Age
International Geophysical Year: 1957

## Slide 3: Space dog - Laika
the occupant of the Soviet spacecraft Sputnik 2 that was launched into outer space on November 3, 1957
Paving the way for human missions

## Slide 4: Explorer I – 1st U.S. Satellite
Explorer 1, was launched into Earth's orbit on a Jupiter C missile from Cape Canaveral, Florida, on January 31, 1958 - Inner belt

## Slide 5: Discovery of the Outer Van Allen RB
Pioneer 3 (launched 6 December 1958) and Explorer IV (launched July 26, 1958) both carried instruments designed and built by Dr. Van Allen. These spacecraft provided Van Allen additional data that led to discovery of a second radiation belt

## Slide 6: Orbits

## Slide 7: Orbits
GEO
Yellow: MEO
Green-dash-dotted line: GPS
Cyan: LEO
Red dotted line: ISS

## Slide 8: Orbits
Different observing assets in near-Earth environment

## Slide 9: Van Allen Probes
Two Spacecraft In an Elliptical Orbit

## Slide 10: MMS (Magnetospheric Multiscale Mission)
Notes: http://mms.space.swri.edu/mission-2.html

## Slide 11: Other types of orbits
Heliocentric orbit: An orbit around the Sun.
STEREO A and STEREO B
Interplanetary space
At different planets

## Slide 12: Importance & Our Increasing Reliance on Space Systems
Scientific Research
  Space science
  Earth science
  Human exploration of space
  Aeronautics and space transportation
Navigation
Telecommunications
Defense
Space environment monitoring
Terrestrial weather monitoring
Courtesy: J. A. Pellish

## Slide 13: Space Weather impacts on spacecraft operation

## Slide 14: Space Environment Model Use in Mission Life Cycle
Mission Concept
Mission Planning
Design
Launch
Operations
Anomaly Resolution
Space Climate
Minimize Risk
Space Weather
Manage Residual Risk
Both
+
in situ
measurements
NASA Space Weather services

## Slide 15: Space Environment & Effects (1)
Mechanism | Effect | Source
Total Ionizing Dose (TID) | Degradation of microelectronics | Trapped protons Trapped electrons Solar protons
Displacement Damage Dose (DDD) | Degradation of optical components and some electronics Degradation of solar cells | Trapped protons Trapped electrons Solar protons Neutrons
Single-Event Effects (SEE) | Data corruption Noise on images System shutdowns Electronic component damage | GCR heavy ions Solar protons and heavy ions Trapped protons Neutrons
Surface Erosion | Degradation of thermal, electrical, optical properties Degradation of structural integrity | Particle radiation Ultraviolet Atomic oxygen Micrometeoroids Contamination

## Slide 16: Space Environment & Effects (2)
Mechanism | Effect | Source
Surface Charging | Biasing of instrument readings Power drains Physical damage | Dense, cold plasma Hot plasma
Deep Dielectric Charging | Biasing of instrument readings Electrical discharges causing physical damage | High-energy electrons
Structure Impacts | Structural damage Decompression | Micrometeoroids Orbital debris
Drag | Torques Orbital decay | Neutral thermosphere
UNCLASSIFIED

## Slide 17: Visual representation of space environment hazards

## Slide 18: Total Dose Effects
Total Ionizing Dose (TID) – cumulative damage resulting from ionization (electron-hole pair formation) causing
  Threshold voltage shifts
  Timing skews
  Leakage currents
Displacement Damage Dose (DDD) – cumulative damage resulting from displacement of atoms in semiconductor lattice structure causing:
  Carrier lifetime shortening
  Mobility degradation
0
2
4
6
8
10
12
14
0
2
4
6
8
10
Total Dose [krad(Si)]
Voltage During Erase Function
Failed to erase
Solar Array Degradation
128 Mb Samsung Flash Memory
DDD can also be referred to in the context of
Non-Ionizing Energy Loss (NIEL)
CREDIT: NRL & JPL
Messenger, S. R., Summers, G. P., Burke, E. A., Walters, R. J. and Xapsos, M. A. (2001), Modeling solar cell degradation in space: A comparison of the NRL displacement damage dose and the JPL equivalent fluence approaches. Prog. Photovolt: Res. Appl., 9: 103–121. doi: 10.1002/pip.357
Notes: Messenger, S. R., Summers, G. P., Burke, E. A., Walters, R. J. and Xapsos, M. A. (2001), Modeling solar cell degradation in space: A comparison of the NRL displacement damage dose and the JPL equivalent fluence approaches. Prog. Photovolt: Res. Appl., 9: 103–121. doi: 10.1002/pip.357

## Slide 19: Seven types SWx impacts for NASA’s robotic missions
Spacecraft surface charging caused by low-energy (< 100 keV) electrons, which are abundant, for example, in the inner magnetosphere during magnetospheric substorms.
Spacecraft internal electrostatic discharge caused by high-energy electrons (> 100 keV) that exist, for example, in the dynamic outer radiation belt of the Earth.
Single event effects due to high-energy (> 10 MeV) protons and heavier ions generated, for example, in solar flares and in coronal mass ejection (CME) shock fronts.
Total dosage effects caused by cumulative charged particle radiation received by spacecraft.
Increased spacecraft drag caused by the thermal expansion of the Earth’s upper atmosphere during space weather storms.
Communication disruptions between ground stations and spacecraft due to ionospheric irregularities
Attitude control disruptions caused, for example, by large storm-time magnetic field fluctuations in the geostationary orbit.
Feedback from our annual SWx workshop for robotic missions

## Slide 20: Space weather impacts on sc (cont’d)
low-energy protons (< 10 MeV) pose a problem due to trapping into charge-coupled device (CCD) substrates.
 virtually any part of electron and ion spectra ranging from low to relativistic energies can impact spacecraft operations.

## Slide 21: Space Environment Anomalies
According to a study by the Aerospace Corporation the 2 most common types of spacecraft anomalies by far are due to electrostatic discharge (ESD) and single event effects (SEE)
Reported results*:
Anomaly Type: | Number of Occurrences:
ESD | 162
SEE | 85
Total Dose and Damage | 16
Miscellaneous | 36
* H.C. Koons et al., 6th Spacecraft Technology Conference, AFRL-VS-TR-20001578, Sept. 2000

## Slide 22: Surface charging: which can lead to electrostatic discharges (ESD), ESD: can lead to a variety of problems, including component failure and phantom commands in spacecraft electronics [Purvis et al., 1984].
Purvis, C. K., H. B. Garrett, A. C. Wittlesey, and N. J. Stevens (1984),
Design guidelines for assessing and controlling spacecraft charging
effects, NASA Tech. Pap. 2361
https://standards.nasa.gov/documents/detail/3314877
Surface Charging

## Slide 23: Surface Charging
Commercial satellite anomaly
More often in the midnight to morning sector
<100 keV e- distribution: similar behavior as spacecraft anomalies
=> Surface charging might be the main cause of the anomalies.
Choi, H.‐S., J. Lee, K.‐S. Cho, Y.‐S. Kwak, I.‐H. Cho, Y.‐D. Park, Y.‐H. Kim, D. N. Baker, G. D. Reeves, and D.‐K. Lee (2011), Analysis of GEO spacecraft anomalies: Space weather relationships, Space Weather, 9, S06001,doi:10.1029/2010SW000597.
Substorm injections ( Aurora)

## Slide 24
Surface Charging Hazards distribution

## Slide 25: NASA Document on Mitigating Charging Effects
Title: Mitigating In-Space Charging Effects-A Guideline
Document Date: 2011-03-03
Revalid and Reaffirmed Date: 2016-03-03
Revision: A
Organization: NASA

## Slide 26
Ring current model data show same
Galaxy 15 failure on April 5, 2010
- surface charging might play a role
22keV electrons 4/5, 8:16-9:32Z
Galaxy 15 failed approx 9:48Z

## Slide 27: Environmental Source of SEE (single event effects)
Single Event Environments in Space
  Galactic Cosmic Rays
  Solar Particle Events (flare/CME)
  Trapped Protons in the inner belt (1 – 3 RE)
  High energy neutrons

## Slide 28: SEE source in Space
Solar Particle
Events (flare/CME)
Trapped
Particles (SAA)
Galactic
Cosmic Rays
High Energy
Particle
Radiation
Most unpredictable
Acknowledge: Mike Xapsos

## Slide 29: Galactic Cosmic Rays
Galactic cosmic rays (GCR) are high-energy charged particles that originate outside our solar system.
Supernova explosions are a significant source
Anticorrelation with solar activity
More pronounced/intense during solar minimum

## Slide 30: South Atlantic Anomaly
Dominates the radiation environment for altitudes less than about 1000 km.
Caused by tilt and shift of geomagnetic axis relative to rotational axis.
Inner edge of proton belt is at lower altitudes south and east of Brazil.
E.J. Daly et al., IEEE TNS, April 1996

## Slide 31: South Atlantic Anomaly
From SPENVIS, http://www.spenvis.oma.be/
Solar Maximum

## Slide 32: Solar Particle Events
Caused by flare/CME

## Slide 33: Characteristics of SEPs
Elemental composition* (may vary event by event)
  96.4% protons
  3.5% alpha particles
  0.1% heavier ions (not to be neglected!)
Energies: up to ~ GeV/nucleon
Event magnitudes:
  > 10 MeV/nucleon integral fluence: can exceed 109 cm-2
  > 10 MeV/nucleon peak flux: can exceed 105 cm-2s-1

## Slide 34: Solar Cycle Dependence
Most unpredictable

## Slide 35: What is a Single Event Effect?
Single Event Effect (SEE) – any measureable effect in a circuit caused by single incident ion
  Non-destructive – SEU (Single Event Upset), SET (single event transients), MBU (Multiple Bit Upsets), SHE (single-event hard error)
  Destructive – SEL (single event latchup), SEGR (single event gate rupture), SEB (single event burnout)
Destructive event
in a COTS 120V
DC-DC Converter

## Slide 36: Single Event Upsets
SEUs: are soft errors, and non-destructive. They normally appear as transient pulses in logic or support circuitry, or as bitflips in memory cells or registers.

## Slide 37: Destructive SEEs
Several types of hard errors, potentially destructive, can appear:
Single Event Latchup (SEL) results in a high operating current, above device specifications, and must be cleared by a power reset.
Other hard errors include Burnout of power MOSFETS (Metal Oxide Semiconductor Field-Effect Transistor) , Gate Rupture, frozen bits, and noise in CCDs.

## Slide 38: Anomalies March 2012 SWx events SEEs dominate
Quite a few NASA spacecraft experienced anomalies, majority of which are SEEs. Some of them required reset/reboot.
Details to be discussed later.

## Slide 39
Internal Charging
- energetic electrons in the outer radiation belt
CIR HSS geomagnetic storm
CME geomagnetic storms

## Slide 40: Human Safety in Space
GCR
SEP
Johnson Space Center/Space Radiation Analysis Group (SRAG)
Limit: the > 100 MeV flux exceeding 1pfu
(1 pfu = 1 particle flux unit= 1/cm^2/sec/sr)
All clear (EVA –extravehicular activity)

## Slide 41: Space Environment Hazards (different types of charging) for Spacecraft in the near-Earth environment
Van Allen Probes
0
200
400
600
HEO-2 Charging Events
L ~ Equatorial Radial Distance (RE)
HEO
GPS
GEO
0
50
100
150
200
250
CRRES MEP-SEU Anomalies
0
CRRES VTCW Anomalies
Inner
Belt
Slot
Outer Belt
5
10
15
1
2
3
4
5
6
7
8
SEUs
Internal
Charging
Surface
Charging
(Dose behind 82.5 mils Al)
Single Event Effects tend to occur in the inner (proton) belt and at higher L shells when a solar particle event is in progress.
Internal electrostatic discharges (ESD) occur over a broad range of L values corresponding to the outer belt, where penetrating electron fluxes are high (300 keV – few MeV electrons)
Surface ESD tends to occur when the spacecraft or surface potential is elevated: at 2000-0800 local time in the plasma sheet and in regions of intense field-aligned currents (auroral zone) (few eV – 50 keV) - plasma sheet, ring current, aurora zone, magnetosheath
Event Total Dose occurs primarily in orbits that rarely see trapped protons in the 1-20 MeV range (e.g., GEO, GPS) because these are the orbits for which solar particle events and transient belts make up a majority of the proton dose (including displacement damage)
Plasma Sheet
Courtesy: Paul O’Brien

## Slide 42: Operator response to SWx impacts spacecraft specific/instrument specific

## Slide 43
March 7 flares/CMEs

## Slide 44
GOES >10 MeV
13-100 MeV STEREO B
13-100 MeV STEREO A
GOES x-ray
M2.0
VCME=1540 km/s
X1.1
VCME=1360 km/s
X5.4/2200 km/s
X1.3/1800 km/s
M6.3/CME=1125 km/s
M8.4
VCME=1500 km/s
M7.9
VCME=2100 km/s
SEP: proton radiation (flare and CME)

## Slide 45: Major events from the long-lasting AR1429 during March 4 – 28, 2012

## Slide 46
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
Flares of the Major Earth-Facing Events viewed by SDO EVE (x-ray)

## Slide 47
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
Flares of the Major Earth-Facing Events viewed by SDO AIA 131

## Slide 48
Orientation
East 90
West 90
Earth

## Slide 49
M2.0, 2012-03-04
X1.1, 2012-03-05
X5.4/X1.3 2012-03-07
M6.3, 2012-03-09
M8.4, 2012-03-10
M7.9, 2012-03-13
The Corresponding CMEs Associated with the Flares

## Slide 50
STA: 2012-03-18
STA: 2012-03-21
STB: 2012-03-24
STB: 2012-03-26
Backsided events in STEREO EUVI 195A (top) and CME model simulations (bottom)

## Slide 51
2012-03-26 23:12UT
VCME=1500 km/s
13-100 MeV STEREO B
13-100 MeV STEREO A
2012-03-18 00:39UT
VCME=1450 km/s
2012-03-21 07:39 UT
VCME=1550 km/s
2012-03-24 00:39UT
VCME=1600 km/s
Enhanced proton radiation at STEREO A and B from the backsided events.
Notes: Enhanced proton radiation at STEREO A and B from the backsided events.

## Slide 52: Supplementary Material/contact info
View our video, Incredible Active Region 1429: One for the record books, to learn more about the activities from this region from March 4 – March 28, 2012. http://youtu.be/PbyJswbX4VA
This video has been updated at the following link: http://youtu.be/dxl5drPY8xQ (And also available on http://vimeo.com/nasaswc/ar1429)
Summary Video of the March 7, 2012 event
    http://youtu.be/HeoKf6NfEJI
    Full text of event summary
    http://goo.gl/dTnfd
http://swc.gsfc.nasa.gov/main/
NASA Space Weather Center

## Slide 53: Supplementary material
Youtube video from Henry Garrett at JPL - http://www.youtube.com/watch?v=NarzGDuYYX4
2 hour and 40 minutes long
KSC Space weather training materials
http://ccmc.gsfc.nasa.gov/support/SWREDI/training_ksc/