## Slide 1: Validating Thermospheric Neutral Density Models using GEODYN’s Precision Orbit Determination
Z.C. Waldron1, K. Garcia-Sage2, E.K. Sutton1, J.P. Thayer1, V. Ray1,
CCMC, and the GEODYN Teams
    1 CU Boulder Space Weather Technology, Research, and Education Center
    2 NASA Goddard, Space Weather Laboratory, Community Coordinated Modeling Center

## Slide 2
Project Goals
  Develop a methodology and tool that can use GEODYN’s POD to validate upper atmospheric density models
  Allow POD program to access many density models while remaining user-friendly
  Perform a case-study validation using ICESat-2
Contributors
  Space Weather Technology, Research, Education Center (SWx TREC) Gas-Vehicles Interaction Team
  CCMC and the Kamodo Team
  GSFC Geodesy and Geophysics Laboratory
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Image and logo from the ICESat-2 Visualization Gallery
GEODYN ASCII art from an output file

## Slide 3: Validation as Motivation
Leverages the high-precision nature of space geodetic POD, but refashioned to focus on satellite drag and density model validation.
Takes advantage of the global coverage becoming available through other GNSS-enabled satellites
Almost any high-quality POD solution can theoretically be used for density model validation through this new tool
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Animated GIF of the ICESat-2’s Polar Orbit from
the ICESat-2 Visualization Gallery

## Slide 4
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Re-determined orbits:
ICESat-2 Mission POD:
MSIS2
DTM2020
JB2008
TIEGCM
CTIPe
HASDM
Step 1: Prepare GEODYN II for drag study using ICESAT-2 input parameters
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Step 3: Perform the Validation

## Slide 5
Step 1: Prepare GEODYN II for drag study using ICESat-2 input parameters
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Inputs
Outputs
Select density model
GEODYN Program
Pygeodyn Wrapper
PCE Tracking Data
Key
GEODYN
Select Density Model
Input
Setup and Control Files
Output
POD orbit
Pygeodyn
Python wrapper
Input
Tracking Data
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Notes: POD usually refers specifically to orbit fits whose residuals are below a certain threshold (that’s variable but usually cm level). It could be dynamic POD (based on precise force models) or reduced-order (using empirical accelerations like they do for IceSat2). Since you are not trying to minimize the residuals here, I would just call them orbit fits.

## Slide 6
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Inputs
Outputs
Select density model
GEODYN Program
Pygeodyn Wrapper
PCE Tracking Data
Key
GEODYN
Select Density Model
Input
Setup and Control Files
Output
POD orbit
Pygeodyn
Python wrapper
Input
Tracking Data
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
The GEODYN II Software
Precision orbit determination and geodetic parameter estimation tool
Made by the GSFC Geodesy and Geophysics Laboratory
Used on every NASA geodetic Earth and planetary altimeter mission since 1985.
Provides very high-fidelity conservative and non-conservative force modelling
Step 1: Prepare GEODYN II for drag study using ICESat-2 input parameters

## Slide 7
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
The Pygeodyn Wrapper
Makes it easier to use GEODYN for satellite drag studies
Makes it easier to add and run multiple density models
Inputs
Outputs
Select density model
GEODYN Program
Pygeodyn Wrapper
PCE Tracking Data
Key
GEODYN
Select Density Model
Input
Setup and Control Files
Output
POD orbit
Pygeodyn
Python wrapper
Input
Tracking Data
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Step 1: Prepare GEODYN II for drag study using ICESat-2 input parameters

## Slide 8
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Inputs
Outputs
Select density model
GEODYN Program
Pygeodyn Wrapper
PCE Tracking Data
Key
GEODYN
Select Density Model
Input
Setup and Control Files
Pygeodyn
Python wrapper
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Use ICESat-2 POD as PCE Tracking data
Step 1: Prepare GEODYN II for drag study using ICESat-2 input parameters
ICESat-2 POD Solutions as PCE tracking data
Constructed by GEODYN team
Empirical accelerations are used to fit GNSS tracking data
  Very low orbit error at ~1.5cm radial precision
“PCE” = precisely converted elements
  orbit trajectory is used as tracking data
Output
POD orbit
GEODYN
(Empirical accelerations)
Input
Setup and Control Files
Use ICESat-2 POD as PCE Tracking data
Input
GNSS Tracking Data
Constructed by GEODYN team
Notes:   We use the precisely determined orbit trajectories of the Ice, Cloud, and Land Elevation Satellite-2 (ICESat-2) as tracking measurement input to a data-reduction run of GEODYN--- the goal being to assess the ability of different density models to re-determine the orbit of ICESat-2.
  We adopt the term precise conversion of elements (PCE) when using known spacecraft trajectories as the tracking measurement type in GEODYN. Therefore, in future sections we sometimes refer to the ICESat-2 POD solutions as the PCE dataset, and refer to the model assessment GEODYN runs in which PCE is the tracking data type and the density models are compared, as model validation runs.

## Slide 9
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
MSIS2
DTM2020
JB2008
TIEGCM
CTIPe
HASDM
Inputs
Outputs
Select density model
GEODYN Program
Pygeodyn Wrapper
PCE Tracking Data
Key
Pygeodyn
Python wrapper
GEODYN
Select Density Model
Input
Setup and Control Files
Outputs
ICESat-2 POD-based orbit fits for a given density model
Pygeodyn
Python wrapper
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Use ICESat-2 POD as PCE Tracking data
Step 1: Prepare GEODYN II for drag study using ICESAT-2 input parameters
Construct an ICESat-2
POD-based orbit fit using each density model
Semi-empirical models are written directly into the GEODYN source code.
More complex physics-based model outputs are interfaced via Kamodo

## Slide 10
Step 1: Prepare GEODYN II for drag study using ICESAT-2 input parameters
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Step 3: Perform the Validation
MSIS2
DTM2020
JB2008
TIEGCM
CTIPe
HASDM
Key Assumptions
All parameters other than atmospheric density are held constant
Drag coefficient is fixed at
Empirical Accelerations are turned off
Pygeodyn
Python wrapper
GEODYN
Select Density Model
Input
Setup and Control Files
Pygeodyn
Python wrapper
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Outputs
ICESat-2 POD-based orbit fits for a given density model
Use ICESat-2 POD as PCE Tracking data

## Slide 11
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Step 3: Perform the Validation
“True” Orbit Trajectory
Model’s Orbit Trajectory
Orbital
Residuals
For each density model:
MSIS2
DTM2020
JB2008
TIEGCM
CTIPe
HASDM
Step 1: Prepare GEODYN II for drag study using ICESAT-2 input parameters
Pygeodyn
Python wrapper
GEODYN
Select Density Model
Input
Setup and Control Files
Pygeodyn
Python wrapper
Step 2: Use different density models to
re-determine the ICESat-2 orbit using GEODYN
Outputs
ICESat-2 POD-based orbit fits for a given density model
Use ICESat-2 POD as PCE Tracking data
Key Assumptions
All parameters other than atmospheric density are held constant
Drag coefficient is fixed at
Empirical Accelerations are turned off

## Slide 12: Validation Metrics for Model Densities are the In-track Residuals and the In-Track RMS errors
In-track Residuals
  Drag effects are seen most clearly in the in-track direction
  Relative deviations from PCE orbit are treated as a proxy for model densities differing from a true density (unknown)
In-track RMSe
  Indicates how well the output orbit matches the PCE orbit over a given arc. The RMSe is the square root of the variance of the residuals.
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
In-track
tangential to the orbit and always points to the velocity vector
Notes: for a perfect force model (including perfect densities), residuals are minimized. The PCE dataset does that by using empirical accelerations.
*assumed-true density refers to a POD-based model density whose errors have been compensated for by GEODYN’s dynamically reduced empirical accelerations and dense tracking measurements and is assumed to represent the realistic density along the satellite’s orbit.

## Slide 13: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Kp Index
Date
Solar Flux (sfu)
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive

## Slide 14: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive

## Slide 15: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
Majority of the error and variations should be due to drag
Notes: Re-iterate the overall steps and why this works given that the Empirical accelerations were used to account for CD/Force model errors in the original POD

## Slide 16: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
Relative deviations from PCE orbit are treated as a proxy for model densities differing from a true density (unknown)
Majority of the error and variations should be due to drag

## Slide 17: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
Not all deviations in the residuals are due to density, so this is a relative metric rather than absolute
Relative deviations from PCE orbit are treated as a proxy for model densities differing from a true density (unknown)
Majority of the error and variations should be due to drag
Notes: Relative metric rather than absolute
Non-drag errors from mismodeled physics are present, but these are minimized and controlled for in inter-comparison runs.

## Slide 18: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
HASDM outputs densities that are close to the unknown truth, and JB2008 performs the best of the semi-empirical and physics-models
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary

## Slide 19: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
The HASDM densities are closest to the true density (unknown)
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary

## Slide 20: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
The strongly negative in-track residuals of
MSIS2 and TIEGCM
Modeled density to be too high
  Causes more drag acceleration
    Density model orbit is behind the PCE orbit.

## Slide 21: Results and Discussion
Orbit Averaged Density
In-Track
Residuals
In-Track
RMSe
Date
Represents a validation of atmospheric models under the following conditions/assumptions:
  Low-to-minor geomagnetic activity, deep solar minimum
  ICESat-2 orbit altitude of ~496 km
  Method captures large/global scale density variations, of which, drag is most sensitive
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
The strongly positive in-track residuals of DTM2020 and CTIPe
Modeled density to be too low
  Causes less drag acceleration
    Density model orbit is ahead of the PCE orbit

## Slide 22
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary
Ongoing Efforts and Future Work
  Implementing a physical CD model into GEODYN such that a density scaling factor can be extracted
  Add more models: GITM and WAM-IPE
  Expand ICESat-2 time period
  Expanding to new satellites and their POD solutions
Concluding Remarks and Questions
  We show our tool that can use GEODYN’s POD to validate upper atmospheric density models
  Allow POD program to access many density models while remaining user-friendly
  Perform a case-study validation using ICESat-2
    HASDM performs best under these conditions, JB2008 performed 2nd best

## Slide 23
Ongoing Efforts and Future Work
  Implementing a physical CD model into GEODYN such that a density scaling factor can be extracted
  Add more models: GITM and WAM-IPE
  Expand ICESat-2 time period
  Expanding to new satellites and their POD solutions
Concluding Remarks and Questions
  We show our tool can use GEODYN’s POD to validate upper atmospheric density models
  Allow POD program to access many density models while remaining user-friendly
  Perform a case-study validation using ICESat-2
    HASDM performs best under these conditions, JB2008 performed 2nd best
Overview/Goals
Results
Methodology
Ongoing/Future Efforts
Concluding Summary

## Slide 25
3-month result