## Slide 1
The semi-empirical thermosphere model DTM2020
Sean Bruinsma
CNES, Space Geodesy Office
Toulouse, France
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 776287

## Slide 2: Summary
THE DTM2020 MODELS
The DTM2013 model was updated using more and different accelerometer inferred densities, SwarmA, and TLE global mean densities at 250 km
Two models were constructed, as well as a model for the 1s uncertainty:
  an ‘operational’ model: DTM2020_Oper
  a ‘research and operational’ model: DTM2020_Res
The CIRA and the new DTM2020 models were assessed by comparing to density data, also the recently released HASDM database was used as an independent validation
The DTM models, as well as the Whole Atmosphere Model MCM, are available on the SWAMI website and on Github:
http://swami-h2020.eu
Papers:
J. Space Weather Space Clim., https:/doi.org/10.1051/swsc/2021032
J. Space Weather Space Clim., https:/doi.org/10.1051/swsc/2021034

## Slide 3: Two DTM2020 models:
THE DTM2020 MODELS
DTM2020 models are, compared with DTM2013, based on:
More & different data, different preprocessing (satellite model)
All data except GRACE were used without scale factors
Improved data correction and editing
Iterative and sequential model development
“OPERATIONAL”: DTM2020_Oper
same algorithm as DTM2013
drivers: F10.7 & Kp
complete database
“RESEARCH”: DTM2020_Res
different Hp algorithm
drivers: F30 & Hp60
database 2000-2019
Intermediate:
F30 & Kp
Complete DB
DTM2013:
F30 & Kp
‘old’ DB
DTM2019:
F30 & Kp
intermediate DB

## Slide 4: Main density data used in the construction/validation of DTM2020
THE DTM2020 MODELS
(15 years)
Spectrometer data:
Eccentric orbits
Before EUV
No recent data
Biased
Hi-Res accelerometer density observations, but very sparse:
Below 250 km
Above 500 km
For cycle max

## Slide 5: Main density data used in the construction/validation of DTM2020
THE DTM2020 MODELS
Thermosphere = 4D
Density data:
TUD instead of CNES
Smaller densities

## Slide 6: Drivers: F10.7, F30
THE DTM2020 MODELS

## Slide 7: Drivers: F10.7, F30
THE DTM2020 MODELS
Drivers: F10.7, F30 & Kp, Hp

## Slide 8: Drivers: F10.7, F30
THE DTM2020 MODELS
Drivers: F10.7, F30 & Kp, Hp

## Slide 9: Assessment: complete datasets (mean density ratio Obs/Mod)
THE DTM2020 MODELS
 | GOCE | CHAMP | GRACE | SwarmA | Stella | TLE250 (‘00-’13) | HASDM 250 km | HASDM 400 km | HASDM 475 km | Starlette
MSIS00 | 0.82 | 0.69 | 0.75 | 0.89 | 0.86 | 0.94 | 0.95 | 0.87 | 0.83 | 0.90
DTM2013 | 0.79 | 0.76 | 0.76 | 0.76 | 0.76 | 0.93 | 0.95 | 0.95 | 0.90 | 0.78
JB2008 | 0.81 | 0.78 | 0.83 | 0.92 | 0.93 | 0.98 | 1.04 | 0.99 | 0.99 | 0.92
MSIS 2.0 | 0.95 | 0.79 | 0.80 | 0.99 | 0.85 | 1.06 | 1.10 | 0.97 | 0.92 | 0.90
DTM2020_Oper | 0.99 | 0.98 | 1.04 | 1.13 | 1.01 | 1.14 | 1.17 | 1.26 | 1.21 | 1.04
DTM2020_Res | 1.00 | 0.98 | 0.99 | 1.00 | 0.97 | 1.17 | 1.23 | 1.25 | 120 | 1.01
ingested not used
DTM2020: 20-30% smaller than DTM2013
MSIS 2.0: 10-20% smaller than MSIS00
Courtesy of the SET HASDM Database

## Slide 10: GOCE & SwarmA: yearly means
THE DTM2020 MODELS

## Slide 11: GOCE & SwarmA: yearly means
THE DTM2020 MODELS

## Slide 12: HASDM 250 km: yearly means - external validation
THE DTM2020 MODELS
0.96 / 5.1%
1.04 / 12.4%
1.01 / 2.6% (w/o ‘18&’19)
1.17 / 7.0%
1.24 / 4.7%
Courtesy of the SET HASDM Database

## Slide 13: HASDM 250 km: yearly means - external validation
THE DTM2020 MODELS
0.96 / 5.1%
1.04 / 12.4%
1.01 / 2.6% (w/o ‘18&’19)
1.17 / 7.0%
1.24 / 4.7%
Courtesy of the SET HASDM Database

## Slide 14: HASDM 475 km: yearly means - external validation
THE DTM2020 MODELS
0.90 / 8.3%
0.99 / 5.9%* >60% elim
1.22 / 8.0%
1.20 / 7.7%
Courtesy of the SET HASDM Database

## Slide 15: HASDM 475 km: yearly means - external validation
THE DTM2020 MODELS
0.90 / 8.3%
0.99 / 5.9%* >60% elim
1.22 / 8.0%
1.20 / 7.7%
Courtesy of the SET HASDM Database

## Slide 16: Take home message: improved DTM (and MCM) models available
THE DTM2020 MODELS
http://swami-h2020.eu
Fitted to TUD densities without scaling
Densities are 20-30% smaller
StD smaller, correlations higher
But:
Relatively sparse data, uneven distribution
And:
Model is improved, not driver predictions
F30 solar proxy:
https://spaceweather.cls.fr/services/radioflux/
Hp geomagnetic index:
ftp://ftp.gfz-potsdam.de/pub/home/obs/Hpo