## Slide 1
Using GEODYN-POD to Validate
Thermospheric Neutral Density Models
Zachary Waldron, SWxTREC CU Boulder
Katherine Garcia-Sage, NASA GSFC
Jeffrey Thayer, SWxTREC
Eric Sutton, SWxTREC
Vishal Ray, Kayhan Space
Marcin Pilinski, LASP
Tom Berger, SWxTREC
June 6, 2024, CCMC Workshop

## Slide 2: We use the GEODYN-II POD software to assess thermospheric neutral density models
Animated GIF of the ICESat-2’s Polar Orbit from
the ICESat-2 Visualization Gallery
Goals:
  Use POD (via GEODYN) to assess upper atmospheric density models
    Pseudo-predictive and retrospective methods
  Provide a neutral density extraction along the orbit of candidate satellites using POD accelerometry methods (no electrostatic accelerometers needed!)
Image and logo from the ICESat-2 Visualization Gallery
2
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction
 | ICESat-2
Altitude | ~490 km
Period | 94.22 mins
 | ICESat-2
Altitude | ~490 km
Period | 94.22 mins

## Slide 3
GEODYN
High fidelity conservative force modeling
Panel model geometry, timeseries of quaternions
Non-drag, non-conservative forces are consistent across runs
Updated force model to include a physically calculate using DRIA
Orbit Fits
to the PSO
Scaling Factors
Model
Orbit Fits
to the PSO
Scaling Factors
Model
Orbit Fits
to the PSO
Scaling Factors
Model
“Drag Study”
Orbits
Metrics
Model
Precise Orbits
(treated as truth)
Why use GEODYN?
  Very high-fidelity conservative force models
  Relatively high-fidelity non-conservative force modeling
  Long legacy as a space-geodetic POD program
Choose density model
Choose density model
Choose density model
Choose density model
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction
3

## Slide 4: In an orbit prediction/propagation, we want to choose the model that reduces in track error
GEODYN
Propagations
(predictive
capability)
Orbit Fits
(retrospective)
Orbit Fits
to the PSO
Scaling Factors
Residuals, RMS, etc.
Model
Orbit Fits
to the PSO
Scaling Factors
Residuals, RMS, etc.
Model
Orbit Fits
to the PSO
Scaling Factors
Residuals, RMS, etc.
Model
Orbit Fits
to the PSO
Scaling Factors
Residuals, RMS, etc.
Model
Choose density model
Choose density model
Choose density model
Choose density model
Precise Science Orbits
(PSO,
treated as truth)
GEODYN can also be used to extract scaling factors for each model which identify the amount of adjustment needed on the density.
Orbit Fits
to the PSO
Scaling Factors
Model
Orbit Fits
to the PSO
Scaling Factors
Model
Orbit Fits
to the PSO
Scaling Factors
Model
Orbit Propagations
In-track Residuals, RMS, etc.
Model
GEODYN
Choose density model
Choose density model
Choose density model
Choose density model
Precise Orbits
(gives initial conditions and “truth”)
4
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction

## Slide 5: Predictive Exercise: 24-hour Orbit Propagation
Can aid operators in choosing appropriate density model for propagation
This is moving in the direction of offering forecast verification
24-hour Propagations of ICESat-2
JB2008
DTM2020
MSIS2
SET-HASDM
5
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction
Imagine we are back in November 2018…
we have been given an orbit predictive solution
Which density model will give the least in-track error?
In-track residuals are the assessment metric for orbit propagations!

## Slide 6: Retrospective Exercise: 24-hour Orbit Fit
JB2008
DTM2020
MSIS2
SET-HASDM
Some time has passed, and we have received a POD solution of the orbit. We now go back and construct orbit fits using GEODYN
Extract 3-hourly scaling factors that fit the density model orbit to the POD solution
  Shows which model provides the best fit to the true orbit
Density
Scaled Density
Scaling Factor
Kp
0.4
0.5
0.7
0.6
0.8
0.9
6
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction
Scaling factors are the primary assessment metric for retrospective orbit fits
Note that error from the drag coefficient has been minimized by physically calculating CD with DIRA

## Slide 7: Retrospective Exercise: Run scaled densities through a propagation
JB2008
DTM2020
MSIS2
SET-HASDM
Can compare the original density propagations to the scaled density propagations.
Scaled Density Propagations
Unscaled Density Propagation
In-Track Residual (m)
Density
In-Track Residual (m)
Scaled
Density
7
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction

## Slide 8: Retrospective Exercise: Run scaled densities through a propagation
JB2008
DTM2020
MSIS2
SET-HASDM
Can compare the original density propagations to the scaled density propagations.
Scaled Density Propagations
Unscaled Density Propagation
In-Track Residual (m)
Density
In-Track Residual (m)
Scaled
Density
8
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction

## Slide 9: This procedure has been done for 6-months and is being expanded
JB2008
DTM2020
MSIS2
SET-HASDM
Assessments for 6-months of ICESat-2
  Propagation Analysis
    In-track Residuals and RMSe
  Retrospective Analysis
    Model Scaling Factors
    Scaled Densities
    Extracted Weighted Average Scaled Density
6-Month Retrospective with ICESat-2
9
Overview/Goals
Predictive ex.
GEODYN Desc.
Retrospective ex.
Density Extraction

## Slide 10: Summary
10
We can use POD solutions and methods to
  assess and validate neutral density models
  scale the density models and retrieve an along orbit density estimates
Our results are coming to CAMEL
Future work
  Expand ICESat-2 time-period
  Cross validation with GRACE-FO
  Apply method to commercial constellations
  Apply method to physics-based models
Thank You!

## Slide 11: BACKUP SLIDES

## Slide 12
ICESat-2 (POD Accelerometry)
vs
GFO (Electrostatic Accelerometer)
 | ICESat-2 | GRACE-FO-C
Perigee | 479 km | ~481.7 km
Apogee | 482 km | ~506.3 km
Period | 94.22 mins | 94.5 mins
 | ICESat-2 | GRACE-FO-C
Perigee | 479 km | ~481.7 km
Apogee | 482 km | ~506.3 km
Period | 94.22 mins | 94.5 mins
Overview
GEODYN Description
Predictive Exercise
ICESat-2 as Density Extraction
Retrospective Exercise
Orbit Average Density (kg/m3)
Percent Difference
Kp

## Slide 13: 24-Hour Propagations of ICESat-2, Unscaled Density
JB2008
DTM2020
MSIS2
SET-HASDM

## Slide 14
JB2008
DTM2020
MSIS2
24-Hour Propagations of ICESat-2, Scaled Density

## Slide 15: Updated GEODYN’s Drag Force Model

## Slide 16: Visualize the scaling process, step-by-step
Model Densities along ICESat2’s Orbit
Scaling Factors, 3-hourly
Scaled Model Densities
Ensemble Weighted Average
Determine the model densities from along the orbit of ICESat-2
3-hour scaling factors from GEODYN. DRIA is used to calculate in the drag force model. The DRAG card in GEODYN becomes a scaling term to be adjusted from 1.0 using the batch least squares reduction.
Densities are scaled and an ensemble weighted average is calculated. The ensemble weighted average is our estimated density extraction.

## Slide 17
Changes in ICESat-2 attitude mode as depicted by the
Nov 2018
Dec 2018
Jan 2019
Feb 2019
Mar 2019
Apr 2019
Scaling Factors
JB2008
DTM2020
MSIS2