## Slide 1
MESSENGER: Effects of AR1429
Robert E. Gold, and the MESSENGER Team
Johns Hopkins University Applied Physics Laboratory, Laurel, MD 20723, USA

## Slide 2
…is the 7th Discovery Mission
Discovery began as a NASA Program in FY 1994.
Program goal is frequent, small, scientifically focused missions.
  Missions are led by a Principal Investigator
Mission proposals are competed and undergo rigorous scientific and technical reviews.
Deep Impact
Mars Pathfinder
Stardust
NEAR
Lunar Prospector
Genesis
MESSENGER
CONTOUR
Dawn
Kepler

## Slide 3
Principal Investigator Sean C. Solomon, Carnegie Institution of Washington
Science Team: 47 scientists from 21 institutions
Project Management: APL
Spacecraft Development/Operations: APL
Propulsion: Aerojet
Structure: Composite Optics
Instruments: APL, Goddard Space Flight Center, University of Colorado Laboratory for Atmospheric and Space Physics, University of Michigan Space Physics Research Laboratory
Team Members
Sponsor
NASA Headquarters Science Mission Directorate Discovery Program Office

## Slide 4
Mercury is a Planet of Extremes
Highest uncompressed density
Highest diurnal variation in temperature • 470 to -185 °C (875 to -300 °F)
Only solar system object in 3:2 spin-orbit resonance • Mercury solar day lasts 2 Mercury years
Geological history ended earliest among the terrestrial planets
Smallest planet with global magnetic field
Most Earth-like magnetosphere

## Slide 5
Why is Mercury so dense?
What is the geologic history of Mercury?
What is the nature of Mercury’s magnetic field?
What is the structure of Mercury’s core?
What are the unusual materials at Mercury’s poles?
What volatiles are important at Mercury?
Science Questions
MESSENGER Objectives
Map the elemental and mineralogical composition of Mercury’s surface
Globally image the surface at a resolution of hundreds of meters or better
Determine the structure of the planet’s magnetic field
Measure the libration amplitude and gravitational field structure
Determine the composition of the radar-reflective materials at Mercury’s poles
Characterize exosphere neutrals and accelerated magnetosphere ions

## Slide 6
MESSENGER’s journey
to Mercury
over 15 trips around the Sun
Notes: 7.9 Billion km journey (1 AU ~ 150 Million km)
MESSENGER needs to speed up to catch Mercury
- Mercury orbital velocity about 48 km/s versus Earth’s orbital velocity of 30 km/s

## Slide 7: Technology Challenges
Severe thermal environment
  >14 kW/m2 thermal input at Mercury (>130 W/ft2)
  Front of S/C > 360° C (680° F)
  S/C can be sandwiched between Sun and planet
  Desire to use standard space electronics
Extreme propulsion required
  > 2300 ms-1 (5150 mph) in-space propulsion to get into Mercury orbit
  Implies very tight mass constraints
Power generation at high temperatures
  Solar panels can reach 270° C (520° F)
Communications reliability
  Keep antenna from thermal extremes
  Return > 75 Gbits from Mercury
Need to operate cryocooled detector at Mercury

## Slide 8
Ceramic cloth sunshade
Low mass, carbon fiber structure
3 large custom propellant tanks
Phased array high-gain antenna
Solar panels are 2/3 mirrors
Custom aluminum launch vehicle adapter
667-N bi-prop thruster
Key Characteristics:
1100 kg total mass
2300 m/s V capable
>720 W orbit power
Spacecraft Enabling Technologies

## Slide 9: Comprehensive Payload
Mercury Atmospheric and Surface Composition Spectrometer (MASCS)
Gamma-Ray Spectrometer (GRNS/GRS)
X-Ray Spectrometer Solar Assembly (XRS/SAX)
Mercury Dual Imaging System (MDIS)
X-Ray Spectrometer Mercury Unit (XRS/MXU)
Data Processing Unit (DPU)
Neutron Spectrometer (GRNS/NS)
Magnetometer (MAG) [at end of boom - not shown]
Energetic Particle Spectrometer (EPPS/EPS)
Fast Imaging Plasma Spectrometer (EPPS/FIPS)
Mercury Laser Altimeter (MLA)

## Slide 10: Spacecraft Must Be Robust
MESSENGER is the innermost space weather monitor in the solar system
  It is vulnerable, being so close to the Sun
An attitude upset at 0.3 – 0.5 AU could quickly be fatal
Solar particle events can be extreme at 0.3 AU
Solar panels will degrade above 180 C
MESSENGER built with rad-hard parts
  Some parts were not as hard as advertised

## Slide 11: Solar Activity
Increased solar activity may lead to temporary data corruption in some instruments during solar particle events, but no permanent damage is anticipated.
  XRS, GRS, and NS all have internal protection that will put them into safe mode during the peak of the events.
  Prevents excessive rates in photo-multiplier tubes and proportional counters
  MASCS and MDIS data may see high backgrounds near the peak of particle events.
  EPS and FIPS can handle very large event rates without problems; rates above those will temporarily saturate the data.
  MAG and MLA are mostly immune to large particle fluxes.
Instrument memory chips have proven to be slightly more vulnerable to bit flips than originally anticipated.
  About a half dozen bit-flip events have been seen in seven years.
  Routine instrument memory checking was instituted during the cruise phase.
  If flipped bits are detected, the instrument is power cycled.

## Slide 12: Active Region 1429
Large active region appeared on the Sun in early March, 2012
Region produced several large flares
  Most intense observed during 8 years of mission
X5.4 flare on March 7 and additional large flares over the next few days
X5.4 X-Ray Flare
>100 MeV Protons

## Slide 13: Effects of AR 1429 Events
MESSENGER well-connected to flare site at ~0.4AU
11 anomalies from solar events
  Temporary effects in attitude control and 5 of the 7 instruments
Some changes were permanent
  Loss of sensitivity, resolution, gain
  Partially fixed by anneal or voltage adjustment
All other subsystems were unaffected

## Slide 14: Specific Effects of AR1429
CCD-based star trackers would not lock onto stars; power cycled to fix
Images had hot pixels and “stars” from penetrating particles
Gamma-ray (GRS) and Neutron (NS)spectrometers had very high counting rates and went into safe mode that turned off high voltages
GRS processor had single event upset in code space and automatically turned instrument off
GRS high-purity germanium detector sustained radiation damage that degraded energy resolution
NS had single event upset outside code area

## Slide 15: Specific Effects of AR1429 -2
Very high NS count rates caused PMT gain shift
Energetic Particles and Plasma Spectrometer (EPPS) had multiple single event upsets
X-Ray Spectrometer (XRS) solar monitor radiation damage increased its leakage current
Mercury Atmospheric and Surface Composition Spectrometer (MASCS) processor RAM had single event upset in code path that turned it off
Magnetometer and Laser Altimeter were unaffected

## Slide 16: Mitigations
Single event upsets were fixed by power cycling or manual content restoration
  No permanent effects
Radiation damage in GRS germanium detector and XRS solar monitor were partially removed by annealing the detectors
  Only partially recoverable
Gain loss in the NS PMT was corrected by raising its voltage

## Slide 17: Affected Subsystems
Data Quality
SEU
Rad Damage
Gain Shift

## Slide 18
What is the Future?
Stretched color image of Mercury
In Mercury orbit ~1.5 yrs (6 Mercury yrs)
MESSENGER continues to discovery the morphology and history of this exciting planet
Just approaching solar max, so future AR1429s may arise

## Slide 19: Follow Mission Progress
http://messenger.jhuapl.edu